## Slide 1
Please check out:
K. Ohmi et al., IPAC2014, THPRI003 & THPRI004
A. Bogomyagkov, E. Levichev, P. Piminov, IPAC2014, THPRI008
Work in progress
FCC-ee accelerator parameters, performance and limitations
M. Koratzinos, University of Geneva, on behalf of the FCC-ee design study
Abstract
CERN has recently launched the Future Circular Collider (FCC) study to deal with all aspects of an ambitious post-LHC possible programme. The emphasis of the study is on a 100 TeV proton collider to be housed in a 80-100 km new ring in the Geneva region. An electron machine will also be considered as a possible intermediate first step (FCC-ee). The study benefits from earlier work done in the context of TLEP and has already published a parameter table, to serve as the basis for the work to be done. The study aims to publish a conceptual design report at around 2018. The recent discovery of a light Higgs boson has opened up considerable interest in circular e+e- Higgs factories around the world. FCC-ee is capable of very high luminosities in a wide centre-of-mass (ECM) spectrum from 90 to 350 GeV. This allows the very precise study of the Z, W and H bosons as well as the top quark, allowing for meaningful precision tests of the closure of the Standard Model .
A more ambitious scheme with great potential at low energies: crab-waist
The crab waist scheme promises large luminosity gains at beam energies of 45 and 80GeV. It avoids the hourglass effect and suppresses betatron coupling resonances allowing to achieve y  0.2
Latest parameter list for FCC-ee at different energies
Major assumptions:
Total SR power dissipation 100MW
Bending radius 11 km
β*y of 1 mm
ξy in the range 0.03 to 0.09
FCC-ee modes of operation
        Higgs factory mode: at 240GeV Ecm above the ZH threshold
        Top quark mode: at 350GeV, so that the Higgs can decay to ttbar
        WW threshold with transverse polarization at 160GeV Ecm : exquisite precision on the W mass
        Z pole running: repeat the whole of the LEP programme in a few minutes
        Z lineshape with transverse polarization: unprecedented precision on lineshape parameters
        Z running with longitudinal polarization: accurate asymmetry measurements
Join us!
The design study is under way and we need experts in all aspects of accelerator design (plus theory, plus experiments).
Number of subscribers to date: 430
Very high luminosity is a trait of circular machines
Above is the total luminosity delivered to four experiments at different beam energies
 | Z | W | H | t
Circumference [km] | 100 | 100 | 100 | 100
Bending radius [km] | 11 | 11 | 11 | 11
Beam energy [GeV] | 45.5 | 80 | 120 | 175
Beam current [mA] | 1450 | 152 | 30 | 6.6
Bunches / beam | 16700 | 4490 | 1360 | 160
Bunch population [1011] | 1.8 | 0.7 | 0.46 | 0.86
Transverse emittance e Horizontal [nm] Vertical [pm] | 29.2 60 | 3.3 7 | 0.94 1.9 | 2 2
Momentum comp. [10-5] | 18 | 2 | 0.5 | 0.5
Betatron function at IP b* Horizontal [m] Vertical [mm] | 0.5 1 | 0.5 1 | 0.5 1 | 1 1
Beam size at IP s* [mm] Horizontal Vertical | 121 0.25 | 26 0.13 | 22 0.044 | 45 0.045
Energy spread [%] Synchrotron radiation Total (including BS) | 0.04 0.06 | 0.07 0.09 | 0.10 0.14 | 0.14 0.16
Bunch length [mm] Synchrotron radiation Total | 1.64 2.56 | 1.01 1.49 | 0.81 1.17 | 1.16 1.27
Energy loss / turn [GeV] | 0.03 | 0.33 | 1.67 | 7.55
SR power / beam [MW] | 50 | 50 | 50 | 50
Total RF voltage [GV] | 2.5 | 4 | 5.5 | 11
RF frequency [MHz] | 800 | 800 | 800 | 800
Longitudinal damping time tE [turns] | 1320 | 243 | 72 | 23
Energy acceptance RF [%] | 2.7 | 7.2 | 11.2 | 7.1
Synchrotron tune Qs | 0.65 | 0.21 | 0.096 | 0.10
Polarization time tp [min] | 11200 | 672 | 89 | 13
Hourglass factor H | 0.64 | 0.77 | 0.83 | 0.81
Luminosity/IP [1034 cm-2s-1] | 28.0 | 12.0 | 6.0 | 1.2
Beam-beam parameter Horizontal Vertical | 0.031 0.030 | 0.060 0.059 | 0.093 0.093 | 0.056 0.056
Luminosity lifetime [min] | 213 | 52 | 21 | 24
We have an aggressive time schedule: detailed technical study in time for the next European strategy update in 2018.
FCC in the Geneva region:
FCC-ACC-SPC-0004 EDMS no 1346082
Very exciting
Very rich scientific programme, testing not only the Higgs sector, but many crucial aspects of the Standard Model
The gain with respect to the baseline design at the Z is a factor of 10!
H
t
W
Z
Z
Z
Final tunnel circumference will depend on:
Physics
Geology
Minimization of cost
ECM Energy [GeV] | 45.5 |  | 80 | 
Collision scheme | Head-on | Crab waist | Head-on | Crab waist
Np [1011] | 1.8 | 1.0 | 0.7 | 4.0
θ [mrad] | 0 | 30 | 0 | 30
σz (SR/total) [mm] | 1.6/3.0 | 2.8/7.6 | 1.0/1.8 | 4.1/11.6
εx [nm] | 29.2 | 0.14 | 3.3 | 0.44
εy [pm] | 60 | 1.0 | 7.0 | 1.0
 | 0.03/0.03 | 0.02/0.14 | 0.06/0.06 | 0.02/0.20
L [1034 cm-1s-1] | 17 | 180 | 13 | 45
ECM Energy [GeV] | 45.5 |  | 80 | 
Collision scheme | Head-on | Crab waist | Head-on | Crab waist
Np [1011] | 1.8 | 1.0 | 0.7 | 4.0
θ [mrad] | 0 | 30 | 0 | 30
σz (SR/total) [mm] | 1.6/3.0 | 2.8/7.6 | 1.0/1.8 | 4.1/11.6
εx [nm] | 29.2 | 0.14 | 3.3 | 0.44
εy [pm] | 60 | 1.0 | 7.0 | 1.0
 | 0.03/0.03 | 0.02/0.14 | 0.06/0.06 | 0.02/0.20
L [1034 cm-1s-1] | 17 | 180 | 13 | 45
Beamstrahlung: a limitation at high energies
Beamstrahlung limits the performance of a circular collider due to beam lifetimes becoming too short. Above a certain energy, it does not allow the machine to run at its theoretical beam-beam limit (red curve). For the FCC-ee parameters, with a momentum acceptance of 2% and beam lifetimes of 300 s (black curve) this crossover is above 120GeV, so only the tt running is affected.