## Slide 1: Measurements of new beta-delayed neutron emission properties around doubly-magic 78Ni (NP1406-RIBF127 proposal)
K.P. Rykaczewski (ORNL Oak Ridge)
in collaboration with
J.L. Tain (IFIC Valencia), R.K. Grzywacz (UT Knoxville)
I. Dillmann (TRIUMF Vancouver) and BRIKEN team
Local coordinator: S. Nishimura
BRIKEN:
nearly all 3He gas available for nuclear spectroscopy
the most powerful ion implantation/decay Si-array AIDA
to be operated at F12 position at Big RIPS

## Slide 2
BRIKEN RIBF127 status
Proposal to measure β1n/β2n emission between 76Co and 92Se got category A in Dec. 2014 (4 days)
All eighty one 3He tubes at 10 atm (17 1” diameter and 64 2” tubes) with their UTK preamps,
ORNL HV system , cables, cable panel etc.. were delivered to RIKEN in April 2015
(after ~2 years of paperwork),
We can supply two clovers for April 2016 test, and later for the main run if CAGRA clovers are
not available (clovers have to travel between ORNL and RIKEN)
We can supply some Cd shielding plates, with 1” HDPE+1 mm Cd
As for today, ORNL/UTK manpower can be available for late April 2016 test run and its preparations
Hybrid 3Hen HDPE-Cd shields
RIKEN April 2015

## Slide 3
Predicted Pβ1n and Pβ2n values
listed according to Moeller 2003
Region of interest (2 Big RIPS settings now, not 3)
Experimental Pβ1n values
are given in black
~ 20 new Pn and 14 new P2n
values

## Slide 4
P1n and P2n values predicted for “our” new nuclei
comparison of Miernik’s EDM 2014 vs Moeller’s QRPA 2003
Larger P1n
Lower P2n

## Slide 5
Reduction of anticipated β2n counts, if P2n is closer to Miernik’s predictions
In most cases we expect few hundred+ of b2n counts, so we should be safe with respect
to counting statistics IF background will not kill us
(efficiencies of 60% beta and 60% 1n were included in rate calculations)
81Cu PM 21%→ 130 counts KM 1. 6% → 10 counts
87Ga PM 13%→ 64 counts KM 7.2% → 35 counts
88Ge PM 0.5% → 270 counts KM < 0.1% → < 54 counts
91As PM 3.2%→ 120 counts KM 0.9% → 34 counts
β – n – n should offer cleaner events in comparison to β – n
(background free spectrum of 11 β – n – n events of 86Ga decay at the HRIBF, Miernik PRL 2013

## Slide 6: Signal to background rate for 78Ni, T1/2=122(5) ms
2 day measurement: about 5600 78Ni ions and about 780 ion-β-correlated neutron counts
total rate ~ 800 ions /s and ~ 50 n/s
distributed over at least ~ 12 000 pixels and 172 3He counters
1 ion per pixel per 15 seconds and about 1 neutron per 20 ms in ALL 172 3He tubes
Nuclear Chemistry Gordon Conference, 2013
78Ni βn-decay
MC simulations
J. L.Tain
78Ni ion-β correlation time of ten half-lives=1.22 s
1 ms thermalization time window for β-n
for large BRIKEN moderator
It gives 5.6 % random background
for the 780 true events of 78Ni-β-n counts
e.g., P1n(78Ni) = 40 (3) %

## Slide 7: 78Ni/79Ni/81Cu setting (R. Grzywacz, N. Fukuda and BigRIPS team)
78Ni
79Ni
81Cu
238U 10 pnA
It is 78Ni/79Ni/81Cu setting
with higher Bρ values with respect
to the optimum 78Ni setting.
It allows us to cut the rates
of less-exotic but very abundant fragments.
82Cu - 7.8% transmission

## Slide 8
Hybrid BRIKEN vs maximized efficiency BRIKEN
82Cu β-decay to s1/2 state in N=51 81Zn, see 2nd BRIKEN workshop
( 80,81,82Cu β-decay experiments were accepted at the HRIBF)
82Cu
Qβ~ 17 MeV
T1/2 ~ 60 ms
82Zn
81Zn
N=51
Sn~ 5 MeV
s1/2
d5/2
0+
(4-,5-)
βn
~ 0.6 MeV
2+
~ 0.7 MeV
YES for hybrid BRIKEN, in particular since the 60% flat efficiency for hybrid BRIKEN
seems to be achievable with our large amount of 3He tubes and large moderator.
For 82Cu, with optimized setting and 20 pnA 238U beam, we can expect about 500 ions in 2 days.
With 5% γ-efficiency and ca 30% P1n to the s1/2 state it gives 3 counts in ion-β-n-γ spectrum.

## Slide 9: Summary I’m impressed by test run results (Alfredo, Gabor, Jose, Shunji.. et al)
ORNL/UTK hardware contribution was delivered to RIKEN in April 2015
Additional contributions like 2 clovers with their HV, and the HDPE-Cd shields possible
Manpower for late April 2016 and later main run “available” so far,
including Shintaro Go – PhD at RIKEN, now a postdoc at UTK.
To be done:
Decide about (hybrid)-BRIKEN design, moderator, Cd shields, clovers
Constant development of data ACQ and on-line analysis
Meeting on data acquisition, in particular AIDA calibration procedures,
and on general evaluation procedures (UTK experts including Shintaro)
Writing a request and filling the forms for BRIKEN test run
Setting up for test run
Asking for main experiment, RIB-127 and 128 , to be run together
Nuclear Chemistry Gordon Conference, 2013