## Slide 1
photo: J. Wenninger
http://cern.ch/fcc
FCC
PS
SPS
LHC
photo: J. Wenninger
Work supported by the European Commission under the HORIZON 2020 projects EuroCirCol, grant agreement 654305; EASITrain, grant agreement no. 764879; ARIES, grant agreement 730871; and E-JADE, contract no. 645479
Status and Plans of the FCC
Michael Benedikt, CERN
on behalf of the FCC collaboration

## Slide 2
FCC integrated program

## Slide 3
The FCC integrated program
inspired by successful LEP – LHC programs at CERN
Comprehensive cost-effective program maximizing physics opportunities
Stage 1: FCC-ee (Z, W, H, ) as Higgs factory, electroweak & and top factory at highest luminosities
Stage 2: FCC-hh (~100 TeV) as natural continuation at energy frontier, with ion and eh options
Complementary physics
Common civil engineering and technical infrastructures
Building on and reusing CERN’s existing infrastructure
FCC integrated project allows seamless continuation of HEP after HL-LHC
FCC-hh
FCC-ee
Notes: The FCC study and program comprises of two accelerators: the Lepton Collider FCC-ee and the Hadron Collider FCC-hh.
The aim of this setup is devise a comprehensive, cost-effective program to maximizing the physics opportunities.

## Slide 4
double ring e+e- collider ~100 km
follows footprint of FCC-hh, except around IPs
asymmetric IR layout & optics to limit synchrotron radiation towards the detector
presently 2 IPs (alternative layouts with 3 or 4 IPs under study), large horizontal crossing angle 30 mrad, crab-waist optics
synchrotron radiation power 50 MW/beam at all beam energies; tapering of arc magnet strengths to match local energy
common RF for running
K. Oide et al.
top-up injection requires booster synchrotron in collider tunnel
FCC-ee basic design choices
FCC-ee: The Lepton Collider, Eur. Phys. J. Spec. Top. 228, 261–623 (2019)
K. Oide et al., Phys. Rev. Accel. Beams 19, 111005 (2016)

## Slide 5
parameter | Z | WW | H (ZH) | ttbar
beam energy [GeV] | 45 | 80 | 120 | 182.5
beam current [mA] | 1390 | 147 | 29 | 5.4
no. bunches/beam | 16640 | 2000 | 393 | 48
bunch intensity [1011] | 1.7 | 1.5 | 1.5 | 2.3
SR energy loss / turn [GeV] | 0.036 | 0.34 | 1.72 | 9.21
total RF voltage [GV] | 0.1 | 0.44 | 2.0 | 10.9
long. damping time [turns] | 1281 | 235 | 70 | 20
horizontal beta* [m] | 0.15 | 0.2 | 0.3 | 1
vertical beta* [mm] | 0.8 | 1 | 1 | 1.6
horiz. geometric emittance [nm] | 0.27 | 0.28 | 0.63 | 1.46
vert. geom. emittance [pm] | 1.0 | 1.7 | 1.3 | 2.9
bunch length with SR / BS [mm] | 3.5 / 12.1 | 3.0 / 6.0 | 3.3 / 5.3 | 2.0 / 2.5
luminosity per IP [1034 cm-2s-1] | 230 | 28 | 8.5 | 1.55
beam lifetime rad Bhabha / BS [min] | 68 / >200 | 49 / >1000 | 38 / 18 | 40 / 18
FCC-ee Collider Parameters

## Slide 6
M. Benedikt, A. Blondel, P. Janot, et al., Nat. Phys. 16, 402-407 (2020), and
European Strategy for Particle Physics Preparatory Group, Physics Briefing Book (CERN, 2019)
FCC-ee: efficient Higgs/electroweak factory
Luminosity L per supplied electrical wall-plug power PWP is shown as a function of centre-of-mass energy for several proposed future lepton colliders.
€200 electricity cost
per Higgs boson
Z
91 GeV
WW
160 GeV
ZH
240 GeV
350-365 GeV

## Slide 7
Marica Biagini
B-factories: KEKB & PEP-II:
double-ring lepton colliders,
high beam currents,
top-up injection
DAFNE: crab waist, double ring
S-KEKB: low by*, crab waist
LEP: high energy, SR effects
VEPP-4M, LEP: precision E calibration
KEKB: e+ source
HERA, LEP, RHIC: spin gymnastics
combining successful ingredients of several recent colliders → highest luminosities & energies
FCC-ee design concept
based on lessons and techniques from past colliders
Marica Biagini

## Slide 8
FCC-ee R&D: RF, cryo-modules, power sources
R&D aimed at improving performance & efficiency and reducing cost:
  improved Nb/Cu coating/sputtering, partner STFC (e.g. ECR fibre growth, HiPIMS)
  new cavity fabrication techniques, partner STFC (e.g. EHF, improved polishing, seamless)
  coating of A15 superconductors (e.g. Nb3Sn), ∙ cryo-module design optimisation
  bulk Nb cavity R&D at FNAL, JLAB, Cornell, also KEK and CEPC/IHEP
  MW-class fundamental power couplers for 400 MHz; ∙ novel high-efficiency klystrons
800 MHz 5-cell Nb
prototype / JLAB
high-efficiency klystron at CERN
New klystron bunching methods:
LHC klystron retrofit as proof of principle for FCC
prototype FCC SRF cavities at JLAB

## Slide 9
parameter | FCC-hh |  | HL-LHC | LHC
collision energy cms [TeV] | 100 |  | 14 | 14
dipole field [T] | 16 |  | 8.33 | 8.33
circumference [km] | 97.75 |  | 26.7 | 26.7
beam current [A] | 0.5 |  | 1.1 | 0.58
bunch intensity [1011] | 1 | 1 | 2.2 | 1.15
bunch spacing [ns] | 25 | 25 | 25 | 25
synchr. rad. power / ring [kW] | 2400 |  | 7.3 | 3.6
SR power / length [W/m/ap.] | 28.4 |  | 0.33 | 0.17
long. emit. damping time [h] | 0.54 |  | 12.9 | 12.9
beta* [m] | 1.1 | 0.3 | 0.15 (min.) | 0.55
normalized emittance [mm] | 2.2 |  | 2.5 | 3.75
peak luminosity [1034 cm-2s-1] | 5 | 30 | 5 (lev.) | 1
events/bunch crossing | 170 | 1000 | 132 | 27
stored energy/beam [GJ] | 8.4 |  | 0.7 | 0.36
FCC-hh (pp) collider parameters

## Slide 10
order of magnitude performance increase in both energy & luminosity
100 TeV cm collision energy (vs 14 TeV for LHC)
20 ab-1 per experiment collected over 25 years of operation (vs 3 ab-1 for LHC)
similar performance increase as from Tevatron to LHC
key technology: high-field magnets
FNAL demonstrator
14.5 T Nb3Sn
from
LHC technology
8.3 T NbTi
via
HL-LHC technology
11 T Nb3Sn
FCC-hh: performance

## Slide 11
16 T dipole design activities and options
Cos-theta
Blocks
Common coils
Short model magnets (1.5 m lengths) will be built until 2025
Swiss contribution
Canted
Cos-theta
H2020
INFN
CEA
CIEMAT
PSI
LBNL
FNAL

## Slide 12
FCC-hh: synchrotron radiation (SR) challenge
test at ANKA/KARA
synchrotron radiation (~ 30 W/m/beam (@16 T field) (cf. LHC <0.2W/m)
~ 5 MW total SR power in arcs from proton beams, emitted inside the cold magnets
strategy: absorption of synchrotron radiation on “beam screen” at higher temperature (> 1.9 K) for cryogenic efficiency; optimum FCC-hh beam screen temperature 40-60 K (cf. LHC 5-20 K) ; beam screen also provides beam vacuum, must suppress electron cloud effect, impedance, etc.
novel “double” beam screen: low impedance, large cooling channels, adequate vacuum pumping, absorption of photo-electrons
beamscreen tests with real SR at KIT
photon spectrum of
ANKA/KARA light source
= photon spectrum in
FCC-hh arcs
I. Bellafont et al., Phys. Rev. Accel. Beams 23, 033201 (2020)
I. Bellafont et al, Phys. Rev. Accel. Beams 23, 043201 (2020)

## Slide 13
FCC implementation - footprint baseline
Present baseline position was established considering:
lowest risk for construction, fastest and cheapest construction
feasible positions for large span caverns (most challenging structures)
More than 75% tunnel in France, 8 (9) / 12 access points in France.
next step: review of surface site locations and machine layout

## Slide 14
Civil Engineering studies
4.5yrs
6.5yrs
Total construction duration 7 years
First sectors ready after 4.5 years

## Slide 15
FCC-tunnel integration in arcs
  FCC-ee FCC-hh
  5.5 m inner diameter

## Slide 16
FCC integral project technical schedule
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17
18
34
35
36
37
38
39
40
41
42
43
15 years operation
Project preparation &
administrative processes
Geological investigations, infrastructure detailed design and tendering preparation
Tunnel, site and technical infrastructure construction
FCC-ee accelerator R&D and technical design
FCC-ee detector construction, installation, commissioning
FCC-ee detector technical design
Permis-sions
Set up of international experiment collaborations, detector R&D and concept development
FCC-ee accelerator construction, installation, commissioning
Funding strategy
Funding and in-kind contribution agreements
FCC-hh detector construction, installation, commissioning
FCC-hh detector R&D, technical design
Update Permissions
FCC-hh accelerator construction, installation, commissioning
FCC-ee dismantling, CE & infrastructure adaptations FCC-hh
Funding and in-kind contribution agreements
~ 25 years operation
FCC-hh accelerator R&D and technical design
Long model magnets, prototypes, preseries
16 T magnet industrialization and series production
Superconducting wire and magnet R&D, short models
70
engineering design, energy efficiency, maintainability
conductors & high-field magnet technology

## Slide 17
FCC-integrated project cost estimate
Total construction cost FCC-ee (Z, W, H) amounts to 10,500 MCHF & 1,100 MCHF (tt).
Total construction cost for subsequent FCC-hh amounts to 17,000 MCHF.
(FCC-hh stand alone cost would be 25 BCHF)
24/06/2020
Snowmass AF-EF Meet 2020
17

## Slide 18
FCC-Conceptual Design Reports:
  Vol 1 Physics, Vol 2 FCC-ee, Vol 3 FCC-hh, Vol 4 HE-LHC
  CDRs published in European Physical Journal C (Vol 1) and ST (Vol 2 – 4)
  EPJ C 79, 6 (2019) 474 , EPJ ST 228, 2 (2019) 261-623 ,
  EPJ ST 228, 4 (2019) 755-1107 , EPJ ST 228, 5 (2019) 1109-1382
Summary documents provided to EPPSU SG
  FCC-integral, FCC-ee, FCC-hh, HE-LHC
  Accessible on http://fcc-cdr.web.cern.ch/
FCC CDR and Study Documentation
>1350 contributors from > 350 institutes,
a truly global effort as suggested by EPPSU 2013

## Slide 19
2020 ESU and plans for 2020 – 2025/26

## Slide 20
From ESPPU 2020 document
      Core sentence and main request “order of the further FCC study”:
      “Europe, together with its international partners, should investigate the technical and financial feasibility of a future hadron collider at CERN with a centre-of-mass energy of at least 100 TeV and with an electron-positron Higgs and electroweak factory as a possible first stage. Such a feasibility study of the colliders and related infrastructure should be established as a global endeavour and be completed on the timescale of the next Strategy update.”

## Slide 21
Feasibility Study of FCC integrated project
Feasibility study to be delivered end 2025 as input for ESPP Update expected for 2026/2027:
Feasibility study of the 100 km tunnel (infrastructure aspects, administrative aspects, local authorities, environment, energy, etc.)
High-risk site investigations included, to confirm principle feasibility
Host-state related processes included to allow start of construction by 2030.
CDR+ for colliders and injectors, including key technologies.
HFM intermediate milestones reached, according to long-term R&D plan.
Physics and experiments CDR + for FCC integrated project.
Financing concept and operation model.
For all these activities the sequential nature of implementation of the colliders and the overall timeline needs to be taken into account!

## Slide 22
CERN resources for period 2021-2025
Total material budget for FCC 75 MCHF, i.e. 15 MCHF/y
Roughly 50% dedicated to host state activities, environmental evaluation, implementation preparation out of which 10-15 MCHF for high-risk site investigations.
Remainder for machine studies, experiment concept studies, technology R&D and technical infrastructure and related collaborations.
Personnel: 30 CERN staff FTE, i.e 150 PY integral.
Other FCC related budget lines in MTP:
  HFM line (16T program) with 75 MCHF M&P
  Dedicated line for RF power source development (HE klystrons) and SRF developments

## Slide 23
CE preparatory activities 2020 - 2030
Schedule of major processes leading to start of construction begin 2030.
For proof of principle feasibility: High risk site investigations 10 - 15 MCHF in 2022/23.
Additional CE investments required in MTP period to allow start of construction in 2030: MSI 45 MCHF, PD 10 MCHF: Total of 55MCHF.

## Slide 24
H2020 FCCIS Design Study
The FCCIS H2020 Design Study project is on one side a co-funding instrument and on the other side a “social promotion” instrument to engage the EC and a community of international partners contractually, including key host state services and offices.
EC co-funding of 2.9 Meuro in the period 11/2020 – 10/2024.
  1.8 Meuro for host state related activities
  1.2 Meuro for FCC-ee optics and machine optimisation
FCCIS follows the EuroCirCol H2020 Design Study that focused on FCC-hh design and technology (2015 – 2019).
The H2020 MarieCurie Training Network EASITrain focuses on FCC cryogenic technologies, SRF and SC magnets and finances 15 Early Stage Researchers (2017 – 2021).

## Slide 25: Beneficiaries
H2020 DS FCC Innovation Study 2020-24
Partners
D.R.R.T. (F)
Etat de Geneve (CH)
DOE (US)
BINP (Ru)
U Oxford (UK)
Beneficiaries
FCCIS Kick-off meeting 9-13 November 2020, in parallel to FCC Physics and Experiments WS
Design optimisation, construction planning, environmental impact assessment, management of
excavation materials, user community building and public engagement, socio-economic impact,…

## Slide 26
Status of Global FCC Collaboration
30
Companies
34
Countries
139
Institutes
EC
H2020
Increasing international collaboration as a prerequisite for success: links with science, research & development and high-tech industry will be essential to further advance and prepare the implementation of FCC

## Slide 27
Spanish participants in FCC Collaboration
CELLS/ALBA, Cerdanyola del Vallès CDTI, Madrid CIEMAT, Madrid
CSIC, Madrid
ICMAB-CSIC, Bellatera IFIC-CSIC, Paterna
IFAE, Bellaterra
UPC, Barcelona URJC, Madrid USC, Santiago de Compostela
Major contributions to HFM, vacuum design, coating technologies & impedance studies…

## Slide 28
1st phase of FCC design study completed → baseline machine designs, performance matching physics requirements, in 4 CDRs
Integrated FCC programme was submitted to the European Strategy Update 2019/20  Request for feasibility study as basis for project decision by 2026/27.
Next steps: concrete local/regional implementation scenario in collaboration with host state authorities, accompanied by machine optimization, physics studies and technology R&D, performed via global collaboration and supported by EC H2020 Design Study FCCIS.
Long term goal: a world-leading HEP infrastructure for the 21st century to push the particle-physics precision and energy frontiers far beyond the present limits.
Status and Outlook

## Slide 29
Scope:
FCC-hh collider key work packages
Optics Design Arc and IR
Cryogenic beam vacuum system design including beam tests at ANKA
16 T dipole design, construction folder demonstrator
EU H2020 Design Study EuroCirCol
European Union Horizon 2020 program
3 MEURO co-funding
Completed in December 2019
15 European beneficiaries & KEK & associated FNAL, BNL, LBL, NHFML
Notes: New slide from Davide.
Showing that conductor development is launched at international level, Russia, Japan, (Korea and Europe in preparation)
Underline importance of that development as main cost driver for the hadron collider machine.

## Slide 30
Administrative processes for project preparatory phase developed.
First review of tunnel placement performed.
Requirements for urbanistic, environmental, economic impact, land acquisition and construction permit related processes defined.
Ongoing: common optimization of collider tunnel and surface site infrastructure implementation.
General secretariat of the region Auvergne-Rhône-Alpes and notified body “Centre d'études et d'expertise sur les risques, l'environnement, la mobilité et l'aménagement” CEREMA
Working group with representatives of federation, canton and state of Geneva and representation of Switzerland at the international organisations and consultancy companies
preparatory work with Host States