## Slide 1: The IDEA detector at the FCC-ee
Status and timelines
Detector requirements
IDEA design
Current R&D
Final remarks
Franco Bedeschi
Spanish network for future colliders
October 7, 2020
Sommario

## Slide 2: Status and timelines
ESU approved by CERN council
    «An electron-positron Higgs factory is the highest-priority next collider………. a feasibility study of the colliders and related infrastructure should be …. completed on the timescale of the next Strategy update.»
Implications on timing for detector R&D:
  Experiment LoI’s by EU strategy 2025/26
    R&D completed – CDR++
  FCCee detector TDR 2028
    Detailed detector design

## Slide 3: Physics at FCC-ee
Higgs factory
  106 e+e- → HZ
EW & Top factory
  3x1012 e+e- → Z
  108 e+e- → W+W- ;
  106 e+e- → tt
Flavor factory
  5x1012 e+e- → bb, cc
  1011 e+e- → 𝛕+𝛕-
Potential discovery of NP
  ALPs, RH ν’s, …
Physics plan still under discussion – Order may change
Z
WW
ZH
t
FCCee
CLIC
CEPC
ILC TDR
ILC upgrade
~100 kHz of physics data at the Z pole

## Slide 4: Requirements for Higgs physics
Tracking:
  Momentum resolution for Z recoil (and Hmm)
    Comparatively low momenta involved  transparency is important
  Vertex resolution/transparency to separate g, c, b, t final states
Calorimetry:
  Jet-jet invariant mass resolution to separate W, Z, H in 2 jets
  Good p0 ID for t and HF reconstruction
ZH (Hmm)
Muon pt
ZH (Zmm)
Muon pt

## Slide 5: Requirements for EWK/HF physics
EWK:
  Extreme definition of detector acceptance
  Extreme EM resolution (crystals) under study
    Improved p0 reconstruction
    Physics with radiative return
HF:
  PID to accurately classify final states and flavor tagging
Other requirements highly overlap with Higgs req.

## Slide 6: Circular vs. Linear
Low field detector solenoid to maximize luminosity
  Optimized at 2 T
  Large tracking volume  calorimeter outside  very thin coil
Beam time structure:
  Short bunch spacing (~ 20-30 ns Z, ~ 1 ms H)
  No large time gap
    Cooling issues for PF calorimeter and vertex detector
    TPC ion backflow
ILC

## Slide 7: IDEA layout
Yoke/m chambers
Yoke/m chambers
Calorimeter
Solenoid
DCH
Small magnet
Small yoke
Tracking  150 mrad
  No material in front of luminometer
Calorimetry  100 mrad

## Slide 8: Detectors & R&D
IDEA concept
Innovative Detector for E+e- Accelerator

## Slide 9: Vertex detector
Transparency:
  Low power (< 20 mW/cm2) to allow air cooling
Resolution:
  5 mm shown by ALICE ITS (30 mm pixels)
  Aim at ~20 mm pixels for ~ 3 mm point resolution
Courtesy of ALICE J.W. van Hoorne

## Slide 10: Silicon detector R&D
Two paths with some overlap:
  DMAPS pixel detector (ARCADIA/LFoundry)
    Test beam with staves by ~ 2023
    INFN-CSN5 call – 2019-2021 (~ 1 M€)
      Additional funds secured also beyond 2021
    MoU in progress with industry and other international labs
  Large area silicon (Pixels and strips)
    First demonstrators use AtlasPix3  modules for mini-staves
    Full system test beam by 2022/23
    New pixel development FCEPCPix1 in AMS
    Passive CMOS micro-strips at Lfoundry
    Large international collaboration:
      China: Harbin, IHEP, NWPU, Shandong, SJTU, Tsingua, UTSTC; Germany: KIT; Italy: Milano, Pisa, Torino; UK: Bristol, Daresbury, Edinburgh, Lancaster, Liverpool, RAL, Sheffield, Warwick

## Slide 11: Drift chamber
High transparency and fast (max drift ~ 400 nsec)
Cluster counting in DCH for good PID resolution
  Excellent K/p separation except 0.75<p<1.05 GeV (blue lines)
  Could recover with timing layer
K/p dN/dx
K/p dE/dx
GeV
3s
Ns K/p separation with TOF over 2 meters
IDEA
90 degree
MS only

## Slide 12: Drift Chamber R&D
Synergic with MEG2/PSI and CMD3 & STC factory/BINP
  Good support from Cremlin+ (2020-2023)
Activities:
  New wire development (eg. C-fiber)
  Low mass mechanics
  Cluster counting electronics
  Simulation and reconstruction SW
Magnetron

## Slide 13: Dual Readout calorimeter
Event by event correction for EM-had fluctuations
  Principle demonstrated by DREAM/RD-52
EM and hadron calorimeter in a single package
  All electronics in back easy to cool and access
NEW: mechanics, SiPM readout, readout electronics
Alternating scintillating and clear fibers in metal matrix

## Slide 14: Dual Readout calorimeter R&D
Collaboration:
  INFN (Italy), RBI (Croatia), Sussex (UK), Korea – (2 M$/5 yr)
  Princeton, Maryland (USA) for potential crystal EM addition
Activities:
  Scalable mechanics
  Scalable SiPM readout
  Performance demonstration with dedicated prototypes
    EM 2021, HAD ~ 2024
  Simulation and reconstruaction SW
C
S
S+C
EM resolution
Hadrons
IDEA Preliminary

## Slide 15: Pre-shower/Muon
Synergy with LHCb upgrade
  Partner companies ELTOS (Italy), TECHTRA (Poland)
Activities:
  Development and industrialization of mRwell chambers
  Optimization in progress for IDEA
    Resistivity and pitch
  Simulation and reconstruction SW

## Slide 16: Software
Significant SW R&D and studies in progress
  Worldwide development of Key4HEP guided by CERN
    DD4HEP, EDM4HEP, ….. for the serious SW developer
  Lot of infrastructure for IDEA:
    DELPHES card available
    Full GEANT simulation in progress
  FCCee physics groups restructured to tackle several “case studies”
    Physics Performance Coordinators recently appointed
      P. Azzi (INFN), E. Perez (CERN)

## Slide 17: Final comments
Summary of main features:
  High precision vertex detector
  High transparency and momentum resolution
    Good integrated PID with cluster counting  even better with timing layer
  Excellent calorimetry  FANTASTIC with crystals
  Light solenoid and minimal yoke
  Tracking muon system
  Excellent performance at all energies: Z, WW, ZH, tt
Based on achievable technologies, but need R&D/SW simulation to finalize, optimize, reduce costs and engineer full detector
Much R&D work in progress supported by several funding sources
Collaboration on all these R&D’s is growing internationally, but there is still ample space for additional contributions

## Slide 18
Additional material

## Slide 19: Special funding (1)
Programs active in 2021:
  ARCADIA (CSN5) - Pixel DMAPS
  Cremlin + (EU) - Drift Chamber/cylindrical mRwell
  FEST (EU) - CEPC: Software/Physics
  FCC-IS - FCC accelerator R&D
Programs seeking approval in 2021:
  HiDRa (CSN5) - Dual Readout calorimetry
  ITN SPIRAL-NET - e+e- collider performance studies

## Slide 20: Special funding (2)
Programs seeking approval in 2021
  AIDAinnova (EU)
    WP 5 – Pixel MAPS – tasks: 5.2.1/ 5.2.2
      ARCADIA/Belle2
    WP 7 – Gas Detectors – tasks: 7.3.2/ 7.4.1
      mRwell chambers/drift chamber readout
    WP 8 – Calorimetria – tasks: 8.4.2
      Dual readout calorimeter
    WP 10 – Cooling per VTX – tasks: 10.2
      Cooling substrates/microcooling
    WP 11 – Microelettronica – tasks: 11.3
      ASICS per mRwell
    WP 12 – Software – tasks: 12.2.1 /12.4.2/ 12.5.2
      Key4HEP/MPGD simulation/Particle flow for Dual readout cal.

## Slide 21: FCC-IS Design Study – just approved by EU-H2020
FCC-IS (Innovation Study) is a design study project: 3M€ for 4 years
Kick-off: 9-10 November 2020
Goal of the FCC-IS study: Carry out the technical design study for a 100 km long luminosity frontier circular collider infrastructure at CERN that will extend Europe’s leadership in the domain of fundamental physics research until the end of the 21st century.
The study focuses on the high priority topics to prepare the ground for a construction project by 2026.
First priority: optimisation of the particle collider design.
It includes both design and prototyping.
NEW!
INFN-LNF participates to FCCIS (Scientific Responsible for INFN: M. Boscolo)
MDI is included in the proposal as well as instabilities and impedance studies
There is usually strong competition for Design Studies. Proposals come from every field of science, including social sciences and humanities. At the last call (November 2019) the success rate was only 18% (10 project approved out of 60 submitted, only 1 for physics selected: FCC-IS).
Examples: at the moment, for accelerators 2 DS have just completed (EuPraxia for a compact plasma-based FEL and EuroCirCol for FCC), ESSnuSB for a neutrino superbeam at ESS is ongoing, FCC-IS, for FCC-ee, has been just approved.
Back

## Slide 22: Crystal option
~20 cm PbWO4
3%/
DR w. filters
Timing layer
  Lyso 20-30 ps
ECAL layer:
  PbWO crystals
  front segment 5 cm (~5.4X0)
  rear segment for core shower
  (15 cm ~16.3X0)
  10x10x200 mm³ of crystal
  5x5 mm² SiPMs (10-15 um)
1x1x5cm3
PbWO
1x1x15cm3
PbWO