## Slide 1: Multiple-cavities interferometric analysis for dark matter axions search based on RF signal cross-correlation processing
José Reina-Valero (1), Iván Martí-Vidal (2), Benito Gimeno (1), Alejandro Díaz-Morcillo (3), Juan Monzó (3), Antonio Lozano (3), Pablo Navarro (3), José Ramón Navarro-Madrid (3)
Instituto de Física Corpuscular (IFIC), CSIC – University of Valencia, 46980 Paterna (Valencia), Spain
(2) Department of Astronomy and Astrophysics, University of Valencia, 46100 Burjassot (Valencia), Spain
(3) Department of Information and Communications Technologies, Technical University of Cartagena, 30203 Cartagena, Spain

## Slide 2
INDE
Motivation
2. Theoretical Formulation
3. Numerical Results
3.1. SNR Improvement
3.2. Directionality and Annual Modulation
4. Conclusions and Future Prospects

## Slide 3
INDEX
Motivation
2. Theoretical Formulation
3. Numerical Results
3.1. SNR Improvement
3.2. Directionality and Annual Modulation
4. Conclusions and Future Prospects

## Slide 4
Motivation
Apply correlation techniques (well-known in radioastronomy) to study systems with low SNR, like in the axion case.

## Slide 5
INDEX
Motivation
2. Theoretical Formulation
3. Numerical Results
3.1. SNR Improvement
3.2. Directionality and Annual Modulation
4. Conclusions and Future Prospects

## Slide 6
Theoretical Formulation: Correlation in Fourier domain
Correlation:
For 2 signals:
For 3 signals:
Power Spectral Density:
observation time

## Slide 7
A
B
FT (A)
FT (B)
AB
Add
Repeat (T)
Sampling frequency following Nyquist criteria:
Theoretical Formulation: Correlation Procedure
Coherent signal
Coherent signal
Gaussian
Noise
Gaussian
Noise

## Slide 8
Theoretical Formulation: BI-RME 3D Method
Equivalent circuit for the axion detection via haloscope
BI-RME 3D method allows us to obtain the detected voltage from the axion-photon decay inside the cavity.
Experimental setup
BI-RME 3D
equivalent to

## Slide 9
Theoretical Formulation: Noisy Resonant Cavity in BI-RME3D
Realistic spectrum of cavity noise
phasor associated to the random electric density current.

## Slide 10
Theoretical Formulation: Cavity Noise in BI-RME3D
Equivalent circuit for the axion + Gaussian noise detection via haloscope

## Slide 11
Theoretical Formulation: Electromagnetic modeling of the cavity
We are going to study a rectangular cavity with the next features (at cryogenic temperature):
= 6.3 kHz
= 1 GHz
= 1.58
= 247.65 mm
= 123.825 mm
= 190 mm
Mode
Critical coupling regime: at resonant frequency (1 GHz)
10 T
σ = 2 S/m

## Slide 12
Theoretical Formulation: Cavity Noise in BI-RME3D (without axion)
Maximum normalized to
3.492 W
ONLY cavity Gaussian noise
= 6.3 kHz
= 1 GHz
= 1.58
= 4 K
σ = 2 S/m

## Slide 13
: Equatorial
LAB
: Galactic
Equatorial
Theoretical Formulation: Axionic halo description in laboratory coordinates
= latitude
= time (day of the year)
Matrix multiplication

## Slide 14
Theoretical Formulation: Axionic halo description in laboratory coordinates
n row of times n component of the velocities summation
N (North): X axis
W (West): Y axis
Z (Zenith): Z axis
longitude
= latitude
= time (day of the year)
= 0.721 days
2π / (0.9973 days)
= 2π / (365 days)
= March 20

## Slide 15
Theoretical Formulation: Maxwell-Boltzmann Bandwidth of the axion
Frequency spectrum of the axion
Shifted Maxwell-Boltzmann
Intrinsic movement
(Maxwell-Boltzmann)
LAB frame velocity
(: Sun’s speed)
;

## Slide 16
Theoretical Formulation: Maxwellian Bandwidth of the axion
Signal lowered to 4 MHz via local oscillator

## Slide 17
Connecting a coaxial probe to the cavity:
Introducing the electric field expression of the mode:
We can obtain an analytical expresión for of the form:
Amplitude ·
Theoretical Formulation: Study of the detected voltage

## Slide 18
Theoretical Formulation: Study of the detected voltage
k = /c ;

## Slide 19
Theoretical Formulation: Electromagnetic modeling for Directional study
3 cavities
C1: d = 0.19 m ( = 1)
C2: d = 2.07 m ( = 11)
C3: d = 3.95 m ( = 21)
· Critical coupling regime: at resonant frequency (1 GHz)
· 10 T
· Lowered to 4 MHz through a LO
Most sensible system for directionality
Mode

## Slide 20
INDEX
Motivation
2. Theoretical Formulation
3. Numerical Results
3.1. SNR Improvement
3.2. Directionality and Annual Modulation
4. Conclusions and Future Prospects

## Slide 21
Numerical Results: 1 cavity
Autocorrelation
x
y
z
Cavity A
Correlator
AA

## Slide 22
Numerical Results: 1 cavity
T = 10 mK
σ = 2 S/m
= 1.58
Iterations:
Autocorrelation

## Slide 23
T = 10 mK
σ = 2 S/m
= 1.58
Numerical Results: 1 cavity
Autocorrelation
Iterations:

## Slide 24
T = 10 mK
σ = 2 S/m
= 1.58
Numerical Results: 1 cavity
Autocorrelation
Iterations:

## Slide 25
T = 10 mK
σ = 2 S/m
= 1.58
Numerical Results: 1 cavity
Autocorrelation
Iterations:

## Slide 26
T = 10 mK
σ = 2 S/m
= 1.58
Numerical Results: 1 cavity
Autocorrelation
Iterations:

## Slide 27
Numerical Results: 2 cavities
Cross - Correlation
x
y
z
Cavity A
Correlator
x
y
z
Cavity B
AB

## Slide 28
T = 10 mK
σ = 2 S/m
= 1.58
Numerical Results: 2 cavities
Cross - Correlation
Iterations:

## Slide 29
T = 10 mK
σ = 2 S/m
= 1.58
Numerical Results: 2 cavities
Cross - Correlation
Iterations:

## Slide 30
T = 10 mK
σ = 2 S/m
= 1.58
Numerical Results: 2 cavities
Cross - Correlation
Iterations:

## Slide 31
T = 300 mK
σ = 2 S/m
= 1.58
Numerical Results: 2 cavities
Cross - Correlation
Iterations:

## Slide 32
T = 300 mK
σ = 2 S/m
= 1.58
Numerical Results: 2 cavities
Cross - Correlation
Iterations:

## Slide 33
Numerical Results: 3 cavities
Cross - Correlation
x
y
z
Cavity A
Correlator
AB
+
BC
+
CA
y
z
Cavity B
y
z
Cavity C
x
x

## Slide 34
T = 300 mK
σ = 2 S/m
= 1.58
Numerical Results: 3 cavities
Cross - Correlation
Iterations:

## Slide 35
Numerical Results: Standard deviation of the Noise for different temperatures

## Slide 36
Numerical Results: SNR Evolution for N cavities oriented into the same direction
1 GHz signal converted to 4 MHz through a LO, with resonant noise at 10 mK
behaviour as expected

## Slide 37
Numerical Results: SNR Evolution
1 GHz signal converted to 4 MHz through a LO, with resonant noise at 10 mK
Good agreement with reference
“Cross-correlation signal processing for axion and WISP dark matter searches”, Ben T. Mc Allister et al., IEEE Transactions on Ultrasonics, Ferroelectrics and Frequency control 66, 2019

## Slide 38
Numerical Results: SNR Evolution
n: Number of cavities
m: Number of times averaged
Good agreement!

## Slide 39
INDEX
Motivation
2. Theoretical Formulation
3. Numerical Results
3.1. SNR Improvement
3.2. Directionality and Annual Modulation
4. Conclusions and Future Prospects

## Slide 40
Numerical Results: Cavities at different positions on the Earth
The first setup was developed by allocating several cavities at different latitudes on Earth
North Pole
Valencia
Equator

## Slide 41
Numerical Results: Cavities C1 at different positions on Earth
No velocity
Valencia
Equator
North Pole
Voltage at resonance = 9.84 · V
No velocity
Valencia
Equator
North Pole

## Slide 42
Numerical Results: Cavities C2 at different places on Earth
No velocity
Valencia
Equator
North Pole
Voltage at resonance = 3.04 · V
No velocity
Valencia
Equator
North Pole

## Slide 43
Numerical Results: Cavities C3 at different places on Earth
Voltage at resonance = 1.21 · V
No velocity
Valencia
Equator
North Pole
No velocity
Valencia
Equator
North Pole

## Slide 44
Numerical Results: Phase-shift between different cavities
Valencia - Eq
North Pole - Eq
Valencia - Eq
North Pole - Eq
C1
C3

## Slide 45
All cavities towards the same direction
3 different positions
Other possibility is three cavities in the same location oriented into three orthogonal directions
(More practical point of view for a realistic experiment)
Valencia
Equator
North Pole
Numerical Results: Phase-shift between different cavities

## Slide 46
z
Zenith
z
Zenith
z
Zenith
x
North
x
North
y
West
Numerical Results: Directional experiment setup
Thus, we will study the next setup:
Zenith – North – West Oriented cavities
By orienting cavities towards different directions we potentiate one different component in each one
x
North

## Slide 47
Numerical Results: Velocity components behaviour in Valencia
Maximum phase-shifts between signals of our directional setup are reached on days in which the difference between velocity components is high

## Slide 48
Numerical Results: Velocity components behaviour in Valencia
Maximum phase-shifts between signals of our directional setup are reached on days in which the difference between velocity components is high
DAY 127

## Slide 49
Zenith - North
West - North
Numerical Results: Phase-shift of the detected voltage in C3 between different cavities (in the day 127)

## Slide 50
Numerical Results: Velocity components behaviour in Valencia
Maximum phase-shifts between signals of our directional setup are reached on days in which the difference between velocity components is high
DAY 308

## Slide 51
Zenith - North
West - North
Numerical Results: Phase-shift in C3 between different cavities (day 308)

## Slide 52
z
Zenith
z
Zenith
z
Zenith
x
North
x
North
y
West
x
North
z
Zenith
x
North
x
North
z
Zenith
x
North
z
Zenith
Numerical Results: Annual Modulation axion signal
Increasing to 6 cavities:

## Slide 53
Numerical Results: Annual Modulation of C1 axion signal
Noisy Data = Axion + Noise

## Slide 54
Numerical Results: Annual Modulation of C3 axion signal
We are able to detect the annual modulation of the signal in the imaginary part for the C3 cavity
Noisy Data = Axion + Noise

## Slide 55
Numerical Results: Annual Modulation of C3 axion signal
We see a clear advantage of studying modulation in imaginary part, since:
Real part variation (cosine): 2nd order perturbation
Imaginary part variation (sine): 1st order perturbation
If you want to study annual modulation
Observe imaginary part

## Slide 56
INDEX
Motivation
2. Theoretical Formulation
3. Numerical Results
3.1. SNR Improvement
3.2. Directionality and Annual Modulation
4. Conclusions and Future Prospects

## Slide 57
Conclusions and future prospects
To sum up all the results obtained, we studied two aspects of the correlation technique applied to the axion detection:
Interferometric analysis of axion detection improvement by means of a multi-cavity system Pre – detection information
Analysis of axion detection with a directional-sensible multi-cavity experiment Post – detection information
Next step: Hypothesis test (how high should SNR be to consider the annual variation a signal)

## Slide 58
THANKS FOR YOUR ATTENTION
jose.reina@uv.es

## Slide 59: Acknowledgments
This work has the support of "Plan de Recuperación, Transformación y Resiliencia (PRTR) 2022 (ASFAE/2022/013)”, funded by Conselleria d’Innovació, Universitats, Ciència i Societat Digital from Generalitat Valenciana, and NextGenerationEU from European Union.

## Slide 60
BACK-UP
SLIDES

## Slide 61
Numerical Results: Annual Modulation of C1 axion signal
Correlation Real Component Maximum Annual Variation for C1 cavity (shortest one) and for two experiments with the mentioned setup:
1st: No phase correction of the results.
2nd: Day-by-day phase correction of the three signals

## Slide 62
Numerical Results: Annual Modulation of C3 axion signal
Correlation Real Component Maximum Annual Variation for C3 cavity (longest one) and for two experiments with the mentioned setup:
1st: No phase correction of the results.
2nd: Day-by-day phase correction of the three signals

## Slide 63
Calculation Procedure: Study of Directionality
Let us assume now that we have two signals with the next structure:
Cross-correlation:
Cross-correlation Fourier transform:

## Slide 64
What purpose may this serve?
Test of whether the observed signal comes from the sky or is a systematic of the experiment Hypothesis test (Next step)
Check if our velocities model is correct
Post-detection information
Numerical Results: Annual Modulation axion signal