## Slide 1: Active Stopper Concepts employing Scintillators
Active stoppers for Decay Experiments
J. Gerl, GSI
March 2025
Universitat de València, Spain

## Slide 2: Content
Active stopper requirements
Why using scintillators
Advanced concepts

## Slide 3: Active stopper for fragmentation facilities
Fragment Separator
degrader
active
stopper
 detectors
 detectors
Aim of an active stopper
stop wanted isotopes in the active volume
provide 3D coordinates of implantation position
provide decent time of implantation
provide rough energy information
measure subsequent β or α decay of an isotope
provide 3D coordinates of decay position
provide precise time of decay
provide decent energy information
correlate implantation and decay event
correlate particle decay with coincident  decay

## Slide 4: The implantation process
1
2
3
heavy ion
1 punch through, 100 MeV range
well localized track,
chance of secondary reactions
2 implantation, 1000 MeV range,
well localized stopping volume,
chance of secondary reactions
3 prompt flash, 1 MeV range
active volume hit by x-rays, -rays, -electrons

## Slide 5: The decay process
224Ac
1
2
3
219Rn
β-decay
E: MeV range, wide distribution
: ≥ µs
long range, random path
α-decay
E: MeV range, discrete lines
: ≥ µs
short range, straight path

## Slide 6: The harsh environment
Fragment separator background
unwanted nuclear species
light charged particles
x-rays, -rays
Electronic noise
electromagnetic interference
detector noise
electronic noise and oscillations
EMI
Fragment Separator

## Slide 7: Implanter requirements
stopping capability for any ion with Z ≥ 6, A ≥ 10 and E ≤ 200 MeV/u
ion detection efficiency as large as possible: > 90%
ion energy resolution enabling distinction of implants and punch-throughs: <10%
ion time resolution enabling decay time measurements: < µs
recovery time after implantation < 0.1ꞏmin : ≈ 100 ns
(active volume / voxel size) < (decay time ꞏ implantation rate):103…104 voxels
decay particle efficiency as large as possible: > 90%
α energy resolution enabling spectroscopy: ≈ 100 keV @ 5 MeV
β energy threshold low enough to avoid substantial efficiency losses: < 100 keV
β time resolution adequate for fast timing  and n measurements: < 400 ps
active implantation cross section fitting to implant distribution: 6 ꞏ 6 cm2 … 24 ꞏ 8 cm2
total size of implanter set-up compact enough for  arrays: < 8ꞏ8ꞏ10 cm3 … 26ꞏ10ꞏ10 cm3
minimal material budget to minimize  absorbtion and scattering: <10% @ 100 keV

## Slide 8: What Si DSSSDs can achieve
stopping capability for any ion with Z ≥ 6, A ≥ 10 and E ≤ 200 MeV/u
ion detection efficiency as large as possible: > 90%
ion energy resolution enabling distinction of implants and punch-throughs: <10%
ion time resolution enabling decay time measurements: < µs ≈ µs
recovery time after implantation < 0.1ꞏmin : ≈ 100 ns > 10 µs
adequate granularity (Vactive / Vvoxel) < ( ꞏ Rimplantation): 103…104 voxels
decay particle efficiency as large as possible: > 90% ≤ 30%
α energy resolution enabling spectroscopy: ≈ 100 keV @ 5 MeV
β energy threshold low enough to avoid substantial efficiency losses: < 100 keV ≈ 100 keV
β time resolution adequate for fast timing  and n measurements: < 400 ps > 2 ns
active implantation cross section fitting to implant distribution: 6 ꞏ 6 cm2 … 24 ꞏ 8 cm2
total size of implanter set-up compact enough for  arrays: < 8ꞏ8ꞏ10 cm3 … 26ꞏ10ꞏ10 cm3
minimal material budget to minimize  absorbtion and scattering: <10% @ 100 keV

## Slide 9: What scintillator detectors may achieve
stopping capability for any ion with Z ≥ 6, A ≥ 10 and E ≤ 200 MeV/u
ion detection efficiency as large as possible: > 90%
ion energy resolution enabling distinction of implants and punch-throughs: <10%
ion time resolution enabling decay time measurements: < µs
recovery time after implantation < 0.1ꞏmin : ≈ 100 ns
adequate granularity (Vactive / Vvoxel) < ( ꞏ Rimplantation): 103…104 voxels
decay particle efficiency as large as possible: > 90% to be shown
α energy resolution enabling spectroscopy: ≈ 100 keV @ 5 MeV to be checked
β energy threshold low enough to avoid substantial efficiency losses: < 100 keV
β time resolution adequate for fast timing  and n measurements: < 400 ps
active implantation cross section fitting to implant distribution: 6 ꞏ 6 cm2 … 24 ꞏ 8 cm2
total size of implanter set-up compact enough for  arrays: < 8ꞏ8ꞏ10 cm3 … 26ꞏ10ꞏ10 cm3
minimal material budget to minimize  absorbtion and scattering: <10% @ 100 keV

## Slide 10: Penetration range of β-particles in plastic
s with E ≤ 500 keV are stopped within 1.5 mm plastic material.
With 3 mm thick plastic sheets (equivalent to 1 mm Si), >90% of s will deposit  100 keV energy.
This leads to a voxel size of 3ꞏ3ꞏ3 mm3 corresponding to > 104 voxels for a 8ꞏ8 cm2 detector cross section.

## Slide 11: Properties of plastic scintillators
Strong quenching of αs
Even stronger quenching of nuclear isotopes
Range of αs < 0.1 mm

## Slide 12: Properties of plastic scintillators
BC404 | 
Light yield (photons/MeV) | 11000
Rise time (ns) | 0.7
Decay time (ns) | 1.8
λ(max. emission) (nm) | 408
Attenuation length (cm) | 160
Density (g/cm2) | 1.02
Perfectly matching with SiPMs
no afterglow
radiation hard

## Slide 13: Inorganic scintillators in comparison to plastic
Pros
higher density  smaller stopping volume for βs, smaller stopping thickness for nuclei
higher light yield  better energy resolution  improved α spectroscopy
Cons (depending on choice)
larger  absorption   detection efficiency reduction
longer decay times  „diluted“ rise times  worse time resolution
afterglow  longer recovery times
higher light attenuation  limited light readout options
mechanically demanding  limited crystal size, less robust
expensive  higher detector cost
Interesting choices
YSO, GAGG, La-GPS, CLYC, CeBr3…

## Slide 14: Non-segmented plate scintillator
bPlast
NUSTAR/DESPEC  AIDA DSSSD + bPlast scintillator
Properties | 
material | BC-400, BC-404
active volume | 80ꞏ80ꞏ3 mm3, 75ꞏ240ꞏ3 mm3
light readout | OnSemi SiPM C-series

## Slide 15: AIDA + bPlast
AIDA + bPlast  coincidence efficiency for fast timing experiments (simulated)
intrinsic bPlast time resolution (multiple SiPM combinations) employing 22Na  source in clean lab environment…
Position resolution
-Implants: ≈ 6 mm
(t distribution ANN)
-Compton e-: ≈ 6mm
(E center-of-gravity)
Time resolution
-Implants: ≈ 30 ps
-,α: ???
For further details see talk by Carole Chatel
works well for high-energy s

## Slide 16: Non-segmented plate scintillator
Pros
excellent time resolution  fast timing capability
50…100 ns recovery time, no afterglow  fast decay capability
low material budget  little  absorption
mechanically robust, cheap
Cons
edge light detection  < 10% photons detectable  limited position resolution  <104 voxels
low density long tracks and escapes at higher β energies  reduced ion-β correlation eff.
Comments
Well suited as fast timing add-on for AIDA
Suitable as stand-alone implanter for α decays (energy resolution to be checked)
Suitable as stand-alone implanter when stacked for  < 5 s or low implant/background rates

## Slide 17: 2D segmented scintillator
VANDLE FRIB
R. Grzywacz et al.
against 418 ps ref. det.
16x16 pixel plastic
48x48x10 mm3 active volume
diffuser plate
8x8 pixel PSPMT
PSPMT dynode for timing

## Slide 18: 2D segmented scintillator
BRIKEN RIBF
>65% beta efficency
For further details see talk by Quanbo Zeng
R. Grzywacz et al.
48x48 pixel YSO
48x48x5 mm3 active volume
glass diffuser plate
8x8 pixel PSPMT
PSPMT dynode for timing

## Slide 19: 2D segmented scintillator
Pros
excellent  detection efficiency
good time resolution  fast timing capability (for neutrons)
good energy resolution  α spectroscopy capability
Excellent position resolution (with inorganic scintillators)
Cons
inorganic scintillators  strong  absorption (for equatorial angles)
plastic  long tracks and escapes at higher β energies  reduced ion-β correlation eff.
long recovery time
Comments
Comes with a variety of scintillators adoptable to specific experiments
Well suited for implant-decay correlations if  absorption is acceptable

## Slide 20: 3D segmented scintillator
Fibers:
St. Gobain cross section 0.5x0.5 mm2
scintillating core 0.4x0.4 mm2
cladding 0.05 mm
Each SiPM reads 4x8 fibers
Fibers are read on both ends
with interleaved SiPMs
 2x2x2 mm3 voxels (granularity 9600)
heavy ion
to be
implanted
SiPM 4x4 mm2
side view
3x20 SiPM
3x19 SiPM
3x20 SiPM
3x19 SiPM
front view
Expected specs:
-Efficiency: >80% at Eβ  500 keV
-Time resolution: <500 ps at Eβ  500 keV
-Energy resolution: <20% at Eβ = 1000 keV
NUSTAR/DESPEC – FIMP (GSI Darmstadt , JSI Ljubljana, IMP Lanzhou)

## Slide 21: 3D segmented scintillator
Geant simulation: Implant – β decay
H. Hao, G. Li
IMP Lanzhou
ion
β
x
z
z
y
x
Exyz(keV)
E ≤ 200 MeV/u
element ID
FIMP enables charged particle tracking: implant, sec. fragm., fission, α, , p, d, t,…

## Slide 22: 3D segmented scintillator
For further details see talks by
Jelena Vesic and Klemen Zagar
FRS
degrader
SC42
SC43


FIMP Box
4 LaBr3
SC41
100Mo
ch10
implant
punch-through
flash
implantation process
β- decay process

## Slide 23: 3D segmented scintillator
Pros
excellent time resolution  fast timing capability
universal charged partcle tracking  valuable novel analysis possibilities
50…100 ns recovery time, no afterglow  fast decay capability
low material budget  little  absorption
Cons
edge light detection  < 10% photons detectable  limited energy resolution
low density long tracks  complex tracking analysis (AI/ML)
Comments
Universal implanter with tracking capability
Under development  Final detector properties not yet known…

## Slide 24: Conclusions
Available implantation decay systems are limited in their properties
On-going R&D work aims to overcome these limitations with scintillator-based systems
Scintillator-based implanter are complementing Si DSSSD stack systems
Fast-timing requirements demand Scintillator-based systems
Latest developments will enable charged particle tracking, which provides possibilities for isotope identification, background event suppression and enhanced efficiency.