## Slide 1
proton decay studies with ACTAR TPC
Active Stoppers for Decay Experiments Workshop
March 2025 – Valencia, Spain
J. Giovinazzo – LP2iB (former CENBG) – Bordeaux
 proton decays physics cases
 time projection chambers / ACTAR TPC
 recent results at GANIL
 signal processing, simulation and analysis
 improvements & perspectives
if time allows…

## Slide 2
proton decay studies with ACTAR TPC
Active Stoppers for Decay Experiments Workshop
March 2025 – Valencia, Spain
J. Giovinazzo – LP2iB (former CENBG) – Bordeaux
Active Stoppers and ancillary detectors
in fragmentation facilities
Electronics and DACQ
Sustainable operation (waveform processing,
noise filtering, AI-based optimizations)
Decay experiments with Active Stoppers
New technologies and materials
 proton decays physics cases
 time projection chambers / ACTAR TPC
 recent results at GANIL
 signal processing, simulation and analysis
 improvements & perspectives
if time allows…

## Slide 3
J. Giovinazzo (LP2iB – CNRS IN2P2 / Univ. Bordeaux)
2025/03 Active Stoppers for Decay Experiments – proton decay studies with ACTAR TPC
physics from beta-delayed proton decay

## Slide 4
J. Giovinazzo (LP2iB – CNRS IN2P2 / Univ. Bordeaux)
2025/03 Active Stoppers for Decay Experiments – proton decay studies with ACTAR TPC
IAS
2p?
QEC
β+ / EC
p
γ
F
GT
p
γ
S2p(Xb)
β-xp: decay spectroscopy
beta decay
Fermi / Gamow Teller
daughter nucleus de-excitation
• gamma transitions
• (multi-)proton emission
detailed decay spectroscopy
 address several topics
simultaneously
very exotic stuff…
 exploration: fragmentation
 details/precision: ISOL
many physics cases
• masses
• isospin symmetry
• weak interaction
• nuclear structure
• deformation
• nuclear astrophysics
• level densities
• excited states lifetimes
• 2-proton decay
• …

## Slide 5
J. Giovinazzo (LP2iB – CNRS IN2P2 / Univ. Bordeaux)
2025/03 Active Stoppers for Decay Experiments – proton decay studies with ACTAR TPC
S2p(Xb)
2p?
p
IAS
QEC
β+ / EC
p
F
GT
γ
γ
β-p: Fermi decay
Isobaric Multiplet Mass Equation (IMME, Wigner, 1957)
charge independent strong nuclear interaction + Coulomb
M(TZ) = a + bTZ + cTZ2
TZ = −2
TZ = −1
TZ = 0
TZ = +1
TZ = +2
T = 2
T = 1
T = 0
T = 2
T = 2
T = 2
T = 2
T = 1
T = 1
β (F)
p
51Fe
(+p)
52Ni
52Co
52Fe
52Mn
52Cr
β(F)-p: IMME (masses)
isospin mixing
worst mass precision !!!
does not compete with
precision (trap) measurements
but the first access to mass for
the most exotic nuclei
( when produced in fragmentation)
less exotic (known)

## Slide 6
J. Giovinazzo (LP2iB – CNRS IN2P2 / Univ. Bordeaux)
2025/03 Active Stoppers for Decay Experiments – proton decay studies with ACTAR TPC
β-p: Fermi decay
56Zn
56Cu
56Ni
56Co
52Fe
56Fe
52Mn
52Co
52Cr
52Ni
48Cr
48V
48Mn
48Ti
48Fe
S.E.A. Orrigo et al., PRC 93 (2016)
experiment @ GANIL / LISE3
comparison of masses
from IMME (exp.) with A.M.E.
S2p(Xb)
2p?
p
IAS
QEC
β+ / EC
p
F
GT
γ
γ
β(F)-p: IMME (masses)
isospin mixing
several cases in A  50 mass region
in C. Dossat et al.,
Nucl. Phys. A 792 (2007)
+ Coulomb displacement energy
(if less than 3 param. of the IMME)
not comparable to
trap measurements !!!

## Slide 7
J. Giovinazzo (LP2iB – CNRS IN2P2 / Univ. Bordeaux)
2025/03 Active Stoppers for Decay Experiments – proton decay studies with ACTAR TPC
S2p(Xb)
2p?
p
IAS
QEC
β+ / EC
p
F
GT
γ
γ
β-p: Fermi decay
proton emission from IAS is forbidden (isospin)
 isospin mixing
 test of INC terms in nucl. interaction (collab. N. Smirnova)
example: TZ = −2 (simple 2-states mixing)
β(F)-p: IMME (masses)
isospin mixing

## Slide 8
J. Giovinazzo (LP2iB – CNRS IN2P2 / Univ. Bordeaux)
2025/03 Active Stoppers for Decay Experiments – proton decay studies with ACTAR TPC
S2p(Xb)
2p?
p
IAS
QEC
β+ / EC
p
F
GT
γ
γ
β-p: Fermi decay
example: case of 44Cr (TZ = −2)
• position of IAS known from gamma
(E666 / LISE, P. Ascher et al.)
• wrong assignment of the proton transition
(beta pile-up, small transition not resolved)
 overestimated isospin mixing
 transition resolved
(E791 + ACTAR TPC, A. Ortega Moral et al.)
proton emission from IAS is forbidden (isospin)
 isospin mixing
 test of INC terms in nucl. interaction (collab. N. Smirnova)
β(F)-p: IMME (masses)
isospin mixing

## Slide 9
J. Giovinazzo (LP2iB – CNRS IN2P2 / Univ. Bordeaux)
2025/03 Active Stoppers for Decay Experiments – proton decay studies with ACTAR TPC
S2p(Xb)
γ
2p?
p
IAS
QEC
β+ / EC
p
γ
F
GT
β-p: astrophysics
states close to the proton emission threshold
decay of 35Ca  proton capture 34Cl(p,g)35Ar
gamma / proton widths in 34Ar
decay of 46Mn  proton capture 45V(p,g)46Cr
 type II supernovae
46Mn
(LISE + ACTAR TPC)
A. Ortega Moral PhD
p / γ: nuclear astrophysics
resonances close to SP
U. Huelva / GANIL coll.
at fragmentation facilities
 impl. in silicon: killed by beta background
 TPC: ok, but need for complementary
gamma detection
preliminary

## Slide 10
J. Giovinazzo (LP2iB – CNRS IN2P2 / Univ. Bordeaux)
2025/03 Active Stoppers for Decay Experiments – proton decay studies with ACTAR TPC
β-p: astrophysics
region Z < 50
 rp-process
(waiting points, e.g. 69Br)
 short half-lives
S2p(Xb)
γ
2p?
p
IAS
QEC
β+ / EC
p
γ
F
GT
p / γ: nuclear astrophysics
resonances close to SP

## Slide 11
J. Giovinazzo (LP2iB – CNRS IN2P2 / Univ. Bordeaux)
2025/03 Active Stoppers for Decay Experiments – proton decay studies with ACTAR TPC
2p?
p
S2p(Xb)
IAS
QEC
β+ / EC
p
γ
F
GT
γ
β(GT)-p: nuclear structure
deformation
comparison
with shell model
β-p: Gamow-Teller strength distribution
B(GT) in light nuclei
decay of 25Si @ GANIL (in-flight)

## Slide 12
J. Giovinazzo (LP2iB – CNRS IN2P2 / Univ. Bordeaux)
2025/03 Active Stoppers for Decay Experiments – proton decay studies with ACTAR TPC
2p?
S2p(Xb)
IAS
QEC
β+ / EC
p
γ
F
GT
γ
p
B(GT)  β-p,2p,3p
ISOLDE & Si-Cube
in 31Ar (Koldste et al., PRC 2014)
Koldste et al., Phys. Lett. B (2014)
from 1p
from 1p+2p
from 1p+2p+3p
p
β(GT)-p: nuclear structure
deformation
β-p: Gamow-Teller strength distribution
B(GT) in light nuclei
decay of 31Ar @ ISOLDE

## Slide 13
J. Giovinazzo (LP2iB – CNRS IN2P2 / Univ. Bordeaux)
2025/03 Active Stoppers for Decay Experiments – proton decay studies with ACTAR TPC
2p?
p
S2p(Xb)
IAS
QEC
β+ / EC
p
γ
F
GT
γ
P. Sarriguren et al., Phys. Rev. C64 (2001)
influence of deformation
on B(GT) distribution
I. Hamamoto et al., Z. Phys. A353 (1995)c
β(GT)-p: nuclear structure
deformation
β-p: Gamow-Teller decay

## Slide 14
J. Giovinazzo (LP2iB – CNRS IN2P2 / Univ. Bordeaux)
2025/03 Active Stoppers for Decay Experiments – proton decay studies with ACTAR TPC
2p?
p
S2p(Xb)
IAS
QEC
β+ / EC
p
γ
F
GT
γ
76Sr J.G. (PhD 1997)
72Kr I. Piqueras et al., EPJA 2003
70Kr A. Vitez-Sveiczer et al., PLB 2022
…
β(GT)-p: nuclear structure
deformation
E. Nacher et al., PRL 92 (2004)
SP
proton
gamma
β-p: Gamow-Teller decay
76Sr

## Slide 15
J. Giovinazzo (LP2iB – CNRS IN2P2 / Univ. Bordeaux)
2025/03 Active Stoppers for Decay Experiments – proton decay studies with ACTAR TPC
γ
γ
IAS
2p?
QEC
β+ / EC
p
F
GT
p
S2p(Xb)
2p (2He) emission
β−2proton emission
E1
E2
E1 + E2 = const
E1
E2
E1 + E2 = const
sequential
direct
sequential emission complete decay scheme
(levels of intermediate nucleus, B(GT),…)
direct emission search for correlation pattern
comparison with ground-state 2P

## Slide 16
J. Giovinazzo (LP2iB – CNRS IN2P2 / Univ. Bordeaux)
2025/03 Active Stoppers for Decay Experiments – proton decay studies with ACTAR TPC
γ
γ
IAS
2p?
QEC
β+ / EC
p
F
GT
p
S2p(Xb)
β−2proton emission
β-2P direct emission never observed
(only sequential decay)
few % direct 2P expected
(B.A. Brown, PRL 1990, calc. from IAS decay, 22Al)
Fynbo et al., N.P. A (2000)
31Ar beta-2p decay (ISOLDE)
 2 energy peaks
 kinematic shift of the 2nd proton
2p (2He) emission

## Slide 17
γ
γ
IAS
2p?
QEC
β+ / EC
p
F
GT
p
S2p(Xb)
2p (2He) emission
β−2proton emission
J. Giovinazzo – DESIR workshop – 27/02-01/03/2024
best candidates for β-2P direct emission ?
 from IAS: 1p forbidden, 2p allowed: TZ < −3/2
 e.g.: 35Ca, 39Ti, 43Cr, …
IβIAS  5% ; R2P/1P  2%  >104 counts for signature
>105 counts for correlations
E791 (LISE+ACTAR TPC)
(A. Ortega Moral et al.)
few events compatible with
β-2p direct emission
 43Cr (and 46Fe?)

## Slide 18
J. Giovinazzo (LP2iB – CNRS IN2P2 / Univ. Bordeaux)
2025/03 Active Stoppers for Decay Experiments – proton decay studies with ACTAR TPC
ISOL vs fragmentation

## Slide 19
J. Giovinazzo (LP2iB – CNRS IN2P2 / Univ. Bordeaux)
2025/03 Active Stoppers for Decay Experiments – proton decay studies with ACTAR TPC
ISOL versus fragmentation
fragmentation
ISOL
Si-tele + Ge
Si-cube + Ge
decay TPC
existing
devices
(+ total absorption spectrometers – not discussed here)
there are specialists in the place !
projectile fragmentation
reaction
(thin target)
spallation or
other reaction
(thick target)
extraction
source
mass separation
(+ purification)
fragments
spectrometer
thick stopper
active
thin catcher
or tape drive
additional
detectors
1050 ns
(10100 ms)
50100 ms
+
+
silicon
or
T.P.C.

## Slide 20
J. Giovinazzo (LP2iB – CNRS IN2P2 / Univ. Bordeaux)
2025/03 Active Stoppers for Decay Experiments – proton decay studies with ACTAR TPC
fragmentation
ISOL
Si-tele + Ge
Si-cube + Ge
decay TPC
existing
devices
beta
detection
multi
proton
only sum
energy
beta
pile-up
energy
& angles
(tracks)
transparent
to beta
separated strips / pixels
energy
threshold
energy
resolution






β
p
p
β
p
p
ε1P70%
ε2P50%
ISOL versus fragmentation: beta-proton detection capabilities
ε100%

## Slide 21
J. Giovinazzo (LP2iB – CNRS IN2P2 / Univ. Bordeaux)
2025/03 Active Stoppers for Decay Experiments – proton decay studies with ACTAR TPC
ISOL versus fragmentation
beam
purity
gamma
proton
detection
multi
proton
IMME
isospin
B(GT)
distrib.
astro.
(low E prot.)
beta
-2P






cocktail beam
multiple isotopes
99.9…%
single isotopes
fragmentation
ISOL
Si-tele + Ge
Si-cube + Ge
decay TPC














existing
devices


## Slide 22
J. Giovinazzo (LP2iB – CNRS IN2P2 / Univ. Bordeaux)
2025/03 Active Stoppers for Decay Experiments – proton decay studies with ACTAR TPC
ISOL versus fragmentation
beam
purity
gamma
proton
detection
multi
proton
IMME
isospin
B(GT)
distrib.
astro.
(low E prot.)
beta
-2P





cocktail beam
multiple isotopes
99.9…%
single isotopes
fragmentation
ISOL
Si-tele + Ge
Si-cube + Ge
decay TPC














existing
devices

requires gamma
detection

?

## Slide 23
J. Giovinazzo (LP2iB – CNRS IN2P2 / Univ. Bordeaux)
2025/03 Active Stoppers for Decay Experiments – proton decay studies with ACTAR TPC
ISOL versus fragmentation
beam
purity
gamma
proton
detection
multi
proton
IMME
isospin
B(GT)
distrib.
astro.
(low E prot.)
beta
-2P





cocktail beam
multiple isotopes
99.9…%
single isotopes
fragmentation
ISOL
Si-tele + Ge
Si-cube + Ge
decay TPC














existing
devices

requires gamma
detection
short half-lives
limitation (100 ms)

?

## Slide 24
J. Giovinazzo (LP2iB – CNRS IN2P2 / Univ. Bordeaux)
2025/03 Active Stoppers for Decay Experiments – proton decay studies with ACTAR TPC
proton(s) radioactivity

## Slide 25
J. Giovinazzo (LP2iB – CNRS IN2P2 / Univ. Bordeaux)
2025/03 Active Stoppers for Decay Experiments – proton decay studies with ACTAR TPC
proton(s) radioactivity
energy
p
A+1,Z+1
A,Z
(+p)
proton charge  Coulomb barrier
if larger than proton separation energy
 metastable state
then tunnel effect
 1-proton radioactivity
beyond the
proton
drip-line

## Slide 26
J. Giovinazzo (LP2iB – CNRS IN2P2 / Univ. Bordeaux)
2025/03 Active Stoppers for Decay Experiments – proton decay studies with ACTAR TPC
proton(s) radioactivity
energy
p
A+1,Z+1
A,Z
(+p)
energy
D
D
2p
pairing effect
(Z is even)
A+2,Z+2
A+1,Z+1
(+p)
A,Z
(+2p)
proton charge  Coulomb barrier
if larger than proton separation energy
 metastable state
then tunnel effect
 1-proton radioactivity
even-Z isotope
1 proton emission forbidden
(so called “true” 2P radioactivity)
drip-line + Coulomb + pairing
 2-proton radioactivity
emitted protons:
- strongly correlated inside the nucleus
- unbound sub-system outside
radius
energy
2P decay

## Slide 27
J. Giovinazzo (LP2iB – CNRS IN2P2 / Univ. Bordeaux)
2025/03 Active Stoppers for Decay Experiments – proton decay studies with ACTAR TPC
proton(s) radioactivity: examples
proton decay of the
10+ isomer in 54Ni
2-proton radioactivity
of 48Ni (and 45Fe)
T1/2  150 ns
T1/2  1-2 ms
production at fragmentation facilities
implantation + decay in active stopper

## Slide 28
J. Giovinazzo (LP2iB – CNRS IN2P2 / Univ. Bordeaux)
2025/03 Active Stoppers for Decay Experiments – proton decay studies with ACTAR TPC
proton(s) radioactivity: examples
proton decay of the
10+ isomer in 54Ni
2-proton radioactivity
of 48Ni (and 45Fe)
T1/2  150 ns
T1/2  1-2 ms
production at fragmentation facilities
implantation + decay in active stopper
+
need for tracking device
GANIL / LISE3
+ ACTAR TPC (2019)
GANIL / LISE3
+ ACTAR TPC (2021)

## Slide 29
J. Giovinazzo (LP2iB – CNRS IN2P2 / Univ. Bordeaux)
2025/03 Active Stoppers for Decay Experiments – proton decay studies with ACTAR TPC
ACTAR TPC tracking detector

## Slide 30
J. Giovinazzo (LP2iB – CNRS IN2P2 / Univ. Bordeaux)
2025/03 Active Stoppers for Decay Experiments – proton decay studies with ACTAR TPC
ACTAR TPC, a versatile detector for nuclear physics
designed as “active target”…
high efficiency, thick target, vertex, tracking,
good energy resolution…
inverse kinematic reactions
unbound resonances, highly excited states
transfer & charge exchange reactions
…and implantation/decay TPC
high efficiency, transp. to beta, low threshold
multi-particle tracking…
charged particles / exotic decay modes
beta-delayed (multi-)proton
particle decay of excited states
3D tracks
reconstruction
capabilities
collaboration (core)
GANIL + Bordeaux
U. Santiago de C.
U. Regina, U. Leuven

## Slide 31
J. Giovinazzo (LP2iB – CNRS IN2P2 / Univ. Bordeaux)
2025/03 Active Stoppers for Decay Experiments – proton decay studies with ACTAR TPC
ACTAR TPC, a 4D detector: tracking and energy
pads plane
(signal collection)
2D digitization
DE(x,y,z)  DE[xi,yj](z)
gas
ionization
particle
track
pads plane
(signal collection)

## Slide 32
J. Giovinazzo (LP2iB – CNRS IN2P2 / Univ. Bordeaux)
2025/03 Active Stoppers for Decay Experiments – proton decay studies with ACTAR TPC
ACTAR TPC, a 4D detector: tracking and energy
pads plane TPC principle
(signal collection)
2D digitization z  t
DE(x,y,z)  DE[xi,yj](z)  DE[xi,yj](t)
gas
ionization
particle
track
pad
signal
pads plane
(signal collection)
ionization
drift
(velocity,,
dispersion)

## Slide 33
J. Giovinazzo (LP2iB – CNRS IN2P2 / Univ. Bordeaux)
2025/03 Active Stoppers for Decay Experiments – proton decay studies with ACTAR TPC
ACTAR TPC, a 4D detector: tracking and energy
pads plane TPC principle time sampling
(signal collection) of signal
2D digitization z  t 3D digitization
DE(x,y,z)  DE[xi,yj](z)  DE[xi,yj](t)  DE[xi,yj,tk]
gas
ionization
particle
track
pad
signal
time sampling
of collected signal
pads plane
(signal collection)
ionization
drift
(velocity,,
dispersion)
GET electronics
3D reconstruction of
ionizations charges along
the particles trajectories
ideal situation
reality is not that
simple…

## Slide 34
J. Giovinazzo (LP2iB – CNRS IN2P2 / Univ. Bordeaux)
2025/03 Active Stoppers for Decay Experiments – proton decay studies with ACTAR TPC
ACTAR TPC, a 4D detector: tracking and energy
ideal case:
• current preamplifier on each channel !
• not easy from electronics point of view
• noisy…
GET electronics based on an existing chip
(AFTER from T2K exp.)

## Slide 35
J. Giovinazzo (LP2iB – CNRS IN2P2 / Univ. Bordeaux)
2025/03 Active Stoppers for Decay Experiments – proton decay studies with ACTAR TPC
ACTAR TPC, a 4D detector: tracking and energy
channel processing (AGET)
CSA
shaper
discri.
analog memory
multiplicity
hit pattern
ADC
TPC
pad signal
ideal case:
• current preamplifier on each channel !
• not easy from electronics point of view
• noisy…
GET electronics based on an existing chip
(AFTER from T2K exp.)
charge preamplifier + shaper
 loss of charge initial distribution
amplitude (A) and timing (T) information
A
T

## Slide 36
J. Giovinazzo (LP2iB – CNRS IN2P2 / Univ. Bordeaux)
2025/03 Active Stoppers for Decay Experiments – proton decay studies with ACTAR TPC
ACTAR TPC, a 4D detector: tracking and energy
channel processing (AGET)
CSA
shaper
discri.
analog memory
multiplicity
hit pattern
ADC
TPC
pad signal
ideal case:
• current preamplifier on each channel !
• not easy from electronics point of view
• noisy…
GET electronics based on an existing chip
(AFTER from T2K exp.)
charge preamplifier + shaper
 loss of charge initial distribution
amplitude (A) and timing (T) information
 decay events in any direction…
A
T

## Slide 37
J. Giovinazzo (LP2iB – CNRS IN2P2 / Univ. Bordeaux)
2025/03 Active Stoppers for Decay Experiments – proton decay studies with ACTAR TPC
ACTAR TPC, a 4D detector: tracking and energy
“standard” analysis
signal amplitude + CFD timing
2D (X,Y) A & T
 2 × 16k = 32k data

## Slide 38
J. Giovinazzo (LP2iB – CNRS IN2P2 / Univ. Bordeaux)
2025/03 Active Stoppers for Decay Experiments – proton decay studies with ACTAR TPC
ACTAR TPC, a 4D detector: tracking and energy
“standard” analysis
signal amplitude + CFD timing
2D (X,Y) A & T
 2 × 16k = 32k data
deconvolution analysis
 response functions for each channel
full 3D (X,Y,T) signal distribution (from FFT)
 512 × 16k = 8000k data
JG, NIM A 2020
analysis / computing cost
×200 !!

## Slide 39
J. Giovinazzo (LP2iB – CNRS IN2P2 / Univ. Bordeaux)
2025/03 Active Stoppers for Decay Experiments – proton decay studies with ACTAR TPC
ACTAR TPC, a 4D detector: tracking and energy
“standard” analysis
signal amplitude + CFD timing
2D (X,Y) A & T
 2 × 16k = 32k data
deconvolution analysis
 response functions for each channel
full 3D (X,Y,T) signal distribution (from FFT)
 512 × 16k = 8000k data
JG, NIM A 2020
problem at large
vertical angles
incorrect
track
length

## Slide 40
J. Giovinazzo (LP2iB – CNRS IN2P2 / Univ. Bordeaux)
2025/03 Active Stoppers for Decay Experiments – proton decay studies with ACTAR TPC
ACTAR TPC, a 4D detector: tracking and energy
“standard” analysis
signal amplitude + CFD timing
2D (X,Y) A & T
 2 × 16k = 32k data
deconvolution analysis
 response functions for each channel
full 3D (X,Y,T) signal distribution (from FFT)
 512 × 16k = 8000k data
JG, NIM A 2020
problem at large
vertical angles

## Slide 41
J. Giovinazzo (LP2iB – CNRS IN2P2 / Univ. Bordeaux)
2025/03 Active Stoppers for Decay Experiments – proton decay studies with ACTAR TPC
metal-core or
multi-layer PCB
+ flexible PCB connection
to readout electronics
16384 pads
(128×128; 2×2 mm2)
collection plane (pads)
drift cage (active volume)
image P. Gangnant, GANIL
image JG / CENBG (2015)
readout electronics
detector
AGET chip
signal sampling
512 @ 1-100 MHz
CoBo modules
MuTAnT
control / acquisition
AsAd boards
clocks distribution
and data concentration
the ACTAR TPC device
“micromegas”
amplification
photo O. Poleshchuk (2017)

## Slide 42
J. Giovinazzo (LP2iB – CNRS IN2P2 / Univ. Bordeaux)
2025/03 Active Stoppers for Decay Experiments – proton decay studies with ACTAR TPC
metal-core or
multi-layer PCB
+ flexible PCB connection to readout electronics
16384 pads
(128×128; 2×2 mm2)
collection plane (pads)
drift cage (active volume)
photo O. Poleshchuk (2017)
image P. Gangnant, GANIL
image JG / CENBG (2015)
readout electronics
detector
AGET chip
signal sampling
512 @ 1-100 MHz
CoBo modules
MuTAnT
control / acquisition
AsAd boards
clocks distribution
and data concentration
the ACTAR TPC device
“micromegas” amplification
JG (2012)
ACTAR TPC @ GANIL / LISE3 (2021)
decay experiments (GANIL/LISE3)
2019: proton radioactivity of 54mNi and isospin symmetry (54mFe)
2021: 2-proton radioactivity of 48Ni & other exotic decays

## Slide 43
J. Giovinazzo (LP2iB – CNRS IN2P2 / Univ. Bordeaux)
2025/03 Active Stoppers for Decay Experiments – proton decay studies with ACTAR TPC
ACTAR TPC decay experiments at GANIL

## Slide 44
J. Giovinazzo (LP2iB – CNRS IN2P2 / Univ. Bordeaux)
2025/03 Active Stoppers for Decay Experiments – proton decay studies with ACTAR TPC
mirror nuclei 54Fe and 54Ni
comparison of 10+ isomers
 near N = Z = 28 shell closures
 test isospin symmetry (breaking)
very few cases for such comparison…
 test coupling to the continuum
54Fe isotope
stable ground state
decay of isomer: known from gamma spectroscopy
54Ni isotope
unstable (proton rich)
 low proton separation energy
decay of isomer
 short half-life
only accessible at fragmentation facilities (+ separator)
 partially known from gamma spectroscopy (GSI /RISING)
 above proton emission threshold
T1/2 = 152(4) ns
stable
unstable
Sp
Sn
proton decay of the 10+ isomer in 54Ni

## Slide 45
J. Giovinazzo (LP2iB – CNRS IN2P2 / Univ. Bordeaux)
2025/03 Active Stoppers for Decay Experiments – proton decay studies with ACTAR TPC
proton decay of the 10+ isomer in 54Ni
T1/2 = 152(4) ns
D. Rudolph et al. Phys. Rev. C 78 (2008)
need for the full
decay scheme
54Ni isomer decay
 above proton emission threshold
but very high angular momentum
1.3 MeV proton (ℓ = 5) deduced from gamma coincidence (RISING)
2.6 MeV proton (ℓ = 7) may exist (not observed)
possible 2P branch (extremely small)

## Slide 46
J. Giovinazzo (LP2iB – CNRS IN2P2 / Univ. Bordeaux)
2025/03 Active Stoppers for Decay Experiments – proton decay studies with ACTAR TPC
proton decay of the 10+ isomer in 54Ni
T1/2 = 152(4) ns
D. Rudolph et al. Phys. Rev. C 78 (2008)
54Ni isomer decay
 above proton emission threshold
but very high angular momentum
1.3 MeV proton (ℓ = 5) deduced from gamma coincidence (RISING)
2.6 MeV proton (ℓ = 7) may exist (not observed)
possible 2P branch (extremely small)
protons detection
• about 0.1% of ions produced in isomeric state
• few MeV proton signal on top of 1 GeV ion signal !
 no standard implantation/decay in a silicon detector
 tracking in a gas detector (ACTAR TPC)
protons emitted out of the ion track
can be observed !
ion
detector
proton
target
separator
cyclotrons
detector
need for the full
decay scheme
need for tracking
detectors

## Slide 47
J. Giovinazzo (LP2iB – CNRS IN2P2 / Univ. Bordeaux)
2025/03 Active Stoppers for Decay Experiments – proton decay studies with ACTAR TPC
54Ni
target
separator
cyclotrons
detector
standard fragmentation production
75 MeV/A 58Ni26+ stable beam, 200 µm nat. Ni target
LISE3 fragment separator
(A,Z) separation, standard ToF – ΔE (Si) ident.
decay of the 10+ isomer in 54Ni: GANIL/LISE experiment (E690)
ion
detector
proton
ACTAR TPC @ LISE
about 0.1% of ions
produced in isomeric state

## Slide 48
J. Giovinazzo (LP2iB – CNRS IN2P2 / Univ. Bordeaux)
2025/03 Active Stoppers for Decay Experiments – proton decay studies with ACTAR TPC
extracting experimental information
time offset
track length
JG et al. NIM A (2022)
• selection of 54Ni and isomer decay events
• identify and separate ion and proton signal
(degraded pad plane)
• drift velocity estimate
TPC principle: ( X , Y , T )  ( X , Y , Z = vd∙T )  track length
from protons signal
• 3D proton tracks fit
trajectory points
+ Bragg peak model
+ signal dispersion
track length  energy
proton start / ion stop time offset  decay time
y
x
t

## Slide 49
J. Giovinazzo (LP2iB – CNRS IN2P2 / Univ. Bordeaux)
2025/03 Active Stoppers for Decay Experiments – proton decay studies with ACTAR TPC
track length ↔ proton energy
E(T1/2)  G(σT)
rad. decay exp. resol.
4D imaging of proton radioactivity
JG et al. NIM A (2022)
original detection/analysis technique
possibilities for short lived decays !

## Slide 50
J. Giovinazzo (LP2iB – CNRS IN2P2 / Univ. Bordeaux)
2025/03 Active Stoppers for Decay Experiments – proton decay studies with ACTAR TPC
track length ↔ proton energy
E(T1/2)  G(σT)
rad. decay exp. resol.
4D imaging of proton radioactivity
1.25 MeV ℓ = 5
2.55 MeV ℓ = 7
L.G. Sarmiento et al., Nature Comm. (2023)
JG et al. Nature Comm. (2021)
JG et al. NIM A (2022)
different detection
efficiency for
1.2 and 2.5 MeV
full simulation
branching ratio
observation of protons with
very high angular momenta
(also case of 53mCo – same exp.
with ℓ = 7 and ℓ = 9)

## Slide 51
J. Giovinazzo (LP2iB – CNRS IN2P2 / Univ. Bordeaux)
2025/03 Active Stoppers for Decay Experiments – proton decay studies with ACTAR TPC
track length ↔ proton energy
E(T1/2)  G(σT)
rad. decay exp. resol.
4D imaging of proton radioactivity
D. Rudolph et al. Phys. Lett. B (2022)
L.G. Sarmiento et al., Nature Comm. (2023)
JG et al. Nature Comm. (2021)
JG et al. NIM A (2022)
1.25 MeV ℓ = 5
2.55 MeV ℓ = 7
different detection
efficiency for
1.2 and 2.5 MeV
full simulation
branching ratio
complete decay scheme
allows for a detailed analysis
 test of isospin non-conserving
terms of the interaction
 constraints on effective isoscalar
and isovector effective charges
from B(E4)

## Slide 52
J. Giovinazzo (LP2iB – CNRS IN2P2 / Univ. Bordeaux)
2025/03 Active Stoppers for Decay Experiments – proton decay studies with ACTAR TPC
2-proton radioactivity
3-body
nature
nuclear
structure
coupling to
continuum
adapted from
M. Pfützner et al. 2023
 drip-line and masses (beyond the « drip-line »)
transition Q-values
 nuclear structure
energies, half-life, levels configuration
 pairing
correlations in energy and angle of emitted protons
 tunnel effect
theoretical descriptions
complex process for theoretical
interpretations / predictions
ideally, taking into account:
• the 3-body decay dynamics
• the nuclear structure (wave functions)
• the coupling to the continuum

## Slide 53
J. Giovinazzo (LP2iB – CNRS IN2P2 / Univ. Bordeaux)
2025/03 Active Stoppers for Decay Experiments – proton decay studies with ACTAR TPC
2-proton radioactivity
p
p
implantation / decay experiments
at fragmentation facilities
 short half-lives
 active stopper
observation: silicon exp.
 standard detectors
 limited info.
(T1/2, Q2P, BR)
correlations: TPC exp.
 tracking devices
 individual protons
information

## Slide 54
J. Giovinazzo (LP2iB – CNRS IN2P2 / Univ. Bordeaux)
2025/03 Active Stoppers for Decay Experiments – proton decay studies with ACTAR TPC
2-proton radioactivity
experimental information: observation (silicon) / correlations (TPC)
• 45Fe: first indirect evidence
(J.G. et al. GANIL 2002,M. Pfützner et al. GSI 2002)
first direct observation (J.G. et al. GANIL 2007)
angular distribution (K. Miernik et al., MSU 2009)
more events, energy sharing (A. Ortega Moral et al., GANIL 2021)
• 54Zn: observation (B. Blank et al. 2005)
few p-p correlations (P. Ascher et al., GANIL 2011)
• 48Ni: indication (B. Blank et al. GANIL 2005)
few p-p correlations (K. Miernik et al., MSU 2007)
few more correlations (A. Ortega Moral et al., GANIL 2021)
Warsaw group exp. at FRIB (2024) – more stat…
• 67Kr: observation (J.G. et al. RIKEN 2015)
 half-life problem…
 deformation / decay mechanism ?
p
p
previous models
fail…

## Slide 55
J. Giovinazzo (LP2iB – CNRS IN2P2 / Univ. Bordeaux)
2025/03 Active Stoppers for Decay Experiments – proton decay studies with ACTAR TPC
2-proton radioactivity
recent theoretical approaches
- hybrid model
(B.A. Brown)
- Gamow Coupled Channels (GCC)
(S. Wang & W. Nazarewicz)
3-body
struct.
cont.
3-body
struct.
cont.
shell model
amplitudes
3-body
dynamics
pure f2
configuration
need for tracking
detectors
experimental
validation !!!
proton-proton correlations predictions
 angular distributions
 energy sharing

## Slide 56
J. Giovinazzo (LP2iB – CNRS IN2P2 / Univ. Bordeaux)
2025/03 Active Stoppers for Decay Experiments – proton decay studies with ACTAR TPC
48Ni decay at GANIL / LISE3 with ACTAR TPC
long beam time, high intensity…
full acceptance of the spectrometer ( ident. problems)
implantation (optimized for 48Ni) in ACTAR TPC
identified stopped 2p /total
in ACTAR decays
45Fe 80 13(+?) 6(+9) / 7(+?)
48Ni 11 6 3 / 5
only few 2P decay events (48Ni & 45Fe)
courtesy of A. Ortega Moral
45Fe
48Ni
…but very small statistics

## Slide 57
J. Giovinazzo (LP2iB – CNRS IN2P2 / Univ. Bordeaux)
2025/03 Active Stoppers for Decay Experiments – proton decay studies with ACTAR TPC
A. Ortega Moral, S. Wang et al., in preparation
half-life and Q-value
48Ni
45Fe
all models fail to reproduce the half-lives with last measured Q-values
 3-body model:
dominant contribution of p3/2 occupancy while expected f7/2 (almost 100% for 48Ni)
(it was ok for 45Fe with Q2P from silicon experiments)
 GCC framework:
increased Vpp favoured for 48Ni, not for 45Fe – but anyway no agreement…
but… systematic trend: Q2P values from TPC experiments smaller
than from silicon experiments
this problem needs
to be clarified !!

## Slide 58
J. Giovinazzo (LP2iB – CNRS IN2P2 / Univ. Bordeaux)
2025/03 Active Stoppers for Decay Experiments – proton decay studies with ACTAR TPC
A. Ortega Moral, S. Wang et al., in preparation
48Ni
45Fe
angular correlations
3-body
GCC
same conclusions as in Miernik et al.
best agreement with 24% of p2
no significant change
favours standard value of Vpp
fairly good agreement with exp.
(2 similar to 3-body)
favours standard value of Vpp
(opposite conclusion than for T1/2)
but similar trend for both models
 confirmation of the persistence
of the shell closure
very low statistics…

## Slide 59
J. Giovinazzo (LP2iB – CNRS IN2P2 / Univ. Bordeaux)
2025/03 Active Stoppers for Decay Experiments – proton decay studies with ACTAR TPC
energy sharing
all models (since prediction in the 1960’s…) suggest
a more favourable equal energy sharing
from barrier penetration considerations
(non-trivial… 2He / p+p tunnelling)
distribution from calculations larger
than experimental ones
3-body model in agreement with data
from K. Miernik et al. (2007)
with O-TPC  poor energy resolution
GCC calculation: no sensitivity to Vpp
(not folded with exp. resol.  worse…)
A. Ortega Moral, S. Wang et al., in preparation
45Fe
what could influence the distribution width ?
mainly (only ?) the barrier height
 requires significantly lower Q2P
 contradiction with T1/2 and exp. TPC/Silicon discrepancy
 proton pair emitted with angular momentum Lpp > 0
(centrifugal barrier) what reason ?...

## Slide 60
J. Giovinazzo (LP2iB – CNRS IN2P2 / Univ. Bordeaux)
2025/03 Active Stoppers for Decay Experiments – proton decay studies with ACTAR TPC
2-proton radioactivity…
• we (I…) thought a consistent description of all aspects ( ) would give a comprehensive picture
• when angular and energy correlations enter the game, we cannot get a satisfying description of
experimental observable:
 contradictory conclusions/trends in models for half-lives and angular distributions
• open question of the energy sharing and the Q-value
 (in principle…) experimental data does not lie… but the systematic difference between TPC
and silicon experiments (despite large uncertainties) must be clarified
 comparison with theory suggests the opposite direction
this is (not) the end !... for experiment & theory
side product: β-xp data
• decay of 44Cr  isospin symmetry
• decay of 46Mn  astrophysics (low energy protons)
• decay of 43Cr  search for direct 2p branch

## Slide 61
J. Giovinazzo (LP2iB – CNRS IN2P2 / Univ. Bordeaux)
2025/03 Active Stoppers for Decay Experiments – proton decay studies with ACTAR TPC
what next ?
the long
journey
from
raw data
to
physics
results
time
out

## Slide 62
J. Giovinazzo (LP2iB – CNRS IN2P2 / Univ. Bordeaux)
2025/03 Active Stoppers for Decay Experiments – proton decay studies with ACTAR TPC
from raw data to physics results

## Slide 63
JG, NIM A 2016
J. Giovinazzo (LP2iB – CNRS IN2P2 / Univ. Bordeaux)
2025/03 Active Stoppers for Decay Experiments – proton decay studies with ACTAR TPC
from raw data to tracks information
raw data
corrected
data
channels signal
corrections
bugs in electronics (CoBo)
“standard” corrections
image JG / CENBG (2015)
detector
CoBo
MuTAnT
DACQ
AsAd

## Slide 64
J. Giovinazzo (LP2iB – CNRS IN2P2 / Univ. Bordeaux)
2025/03 Active Stoppers for Decay Experiments – proton decay studies with ACTAR TPC
from raw data to tracks information
raw data
corrected
data
calibrated
data
signal collection
(detector)
time alignment
(electronics)
image JG / CENBG (2015)
detector
CoBo
MuTAnT
DACQ
AsAd
time alignment
gain matching
electronic
channels
amplitude
time
channels signal
corrections
JG et al., NIM A 2016
JG et al., NIM A 2021

## Slide 65
J. Giovinazzo (LP2iB – CNRS IN2P2 / Univ. Bordeaux)
2025/03 Active Stoppers for Decay Experiments – proton decay studies with ACTAR TPC
from raw data to tracks information
raw data
corrected
data
calibrated
data
image JG / CENBG (2015)
detector
CoBo
MuTAnT
DACQ
AsAd
corrected
signal
time alignment
gain matching
channels signal
corrections
correction of saturated
with unsaturated
template signals
(from same channel)
final signal
corrections
saturation correction
JG et al., NIM A 2021

## Slide 66
J. Giovinazzo (LP2iB – CNRS IN2P2 / Univ. Bordeaux)
2025/03 Active Stoppers for Decay Experiments – proton decay studies with ACTAR TPC
from raw data to tracks information
raw data
corrected
data
calibrated
data
correction of signal induced
on all pads from pad-plane
mesh (micromegas)
amplification (avalanche)
image JG / CENBG (2015)
detector
CoBo
MuTAnT
DACQ
AsAd
final signal
corrections
corrected
signal
time alignment
gain matching
channels signal
corrections
mesh induced signal correction
JG et al., NIM A 2020

## Slide 67
J. Giovinazzo (LP2iB – CNRS IN2P2 / Univ. Bordeaux)
2025/03 Active Stoppers for Decay Experiments – proton decay studies with ACTAR TPC
from raw data to tracks information
raw data
corrected
data
calibrated
data
beam line
detector
events selection
corrected
signal
ion impl.
event
decay
event
energy loss
time-of-flight
ext. trigger
signal in ACTAR TPC
active volume only

## Slide 68
J. Giovinazzo (LP2iB – CNRS IN2P2 / Univ. Bordeaux)
2025/03 Active Stoppers for Decay Experiments – proton decay studies with ACTAR TPC
from raw data to tracks information
raw data
corrected
data
calibrated
data
beam line
detector
events selection
corrected
signal
ion impl.
event
simple track fitting
beam along X axis
- Y(X), T/Z(X) directions
- charge profile model
 stopping point estimate
(identification not
discussed here)

## Slide 69
J. Giovinazzo (LP2iB – CNRS IN2P2 / Univ. Bordeaux)
2025/03 Active Stoppers for Decay Experiments – proton decay studies with ACTAR TPC
from raw data to tracks information
raw data
corrected
data
calibrated
data
beam line
detector
events selection
corrected
signal
ion impl.
event
simple track fitting
beam along X axis
- Y(X), T/Z(X) directions
- charge profile model
 stopping point estimate
defined from
correlation
with decay events
(identification not
discussed here)

## Slide 70
J. Giovinazzo (LP2iB – CNRS IN2P2 / Univ. Bordeaux)
2025/03 Active Stoppers for Decay Experiments – proton decay studies with ACTAR TPC
from raw data to tracks information
raw data
corrected
data
calibrated
data
beam line
detector
events selection
corrected
signal
decay
event
typology / topology analysis
 1p, 2p, 3p, α, junk…
alpha
protons
light
particles
• princ. comp. analysis (signal)
• multi param. conditions
(max./mean ampl./charge,
pads mult, length,…)
• Hough transform
• …
very complex, still “artisanal”
• difficult automation
• need for tools development
- machine learning type ?
- high efficiency required !
y
x

## Slide 71
J. Giovinazzo (LP2iB – CNRS IN2P2 / Univ. Bordeaux)
2025/03 Active Stoppers for Decay Experiments – proton decay studies with ACTAR TPC
from raw data to tracks information
raw data
corrected
data
calibrated
data
beam line
detector
events selection
corrected
signal
decay
event
drift velocity estimate
Δt ↔ Δz
proton 1
proton 2
(1)
(2)
(3)
Δt = tmax – tmin
(1)
(2)
(3)
y
x
t
protons from
54mNi (E690)
beta-proton(s)
from E791
tools such as GARFIELD not
precise enough at low electric fields

## Slide 72
J. Giovinazzo (LP2iB – CNRS IN2P2 / Univ. Bordeaux)
2025/03 Active Stoppers for Decay Experiments – proton decay studies with ACTAR TPC
from raw data to tracks information
raw data
corrected
data
calibrated
data
beam line
detector
events selection
corrected
signal
decay
event
parasitic signal suppression
t
x
t
y
noise or beta signal  spoil track fitting
y
x

## Slide 73
J. Giovinazzo (LP2iB – CNRS IN2P2 / Univ. Bordeaux)
2025/03 Active Stoppers for Decay Experiments – proton decay studies with ACTAR TPC
from raw data to tracks information
raw data
corrected
data
calibrated
data
beam line
detector
events selection
corrected
signal
decay
event
tracks fitting 2D (A+T) / 3D (full)
  • trajectory definition
  start and stop 3D points
  (+ additional control points)
  • Bragg peak model
  projected along the trajectory
  amplitude factor & length fraction
  • dispersion along drift
  • energy deposit from recoil nucleus
  from fit:
   track length (≡ energy), angles (x-p)
  fitted total charge

## Slide 74
J. Giovinazzo (LP2iB – CNRS IN2P2 / Univ. Bordeaux)
2025/03 Active Stoppers for Decay Experiments – proton decay studies with ACTAR TPC
from raw data to tracks information
raw data
corrected
data
calibrated
data
beam line
detector
events selection
corrected
signal
decay
event
tracks fitting 2D (A+T) / 3D (full)
  • trajectory definition
  start and stop 3D points
  (+ additional control points)
  • Bragg peak model
  projected along the trajectory
  amplitude factor & length fraction
  • dispersion along drift
  • energy deposit from recoil nucleus
  from fit:
   track length (≡ energy), angles (x-p)
  fitted total charge
+ large number of parameters
+ data size (full3D fits)
+ standard minimizer (MINUIT)
= very slow processing

## Slide 75
J. Giovinazzo (LP2iB – CNRS IN2P2 / Univ. Bordeaux)
2025/03 Active Stoppers for Decay Experiments – proton decay studies with ACTAR TPC
from tracks to physics
raw data
corrected
data
calibrated
data
beam line
detector
events selection
corrected
signal
decay
event
ion impl.
event
identified (A,Z) implantations

## Slide 76
J. Giovinazzo (LP2iB – CNRS IN2P2 / Univ. Bordeaux)
2025/03 Active Stoppers for Decay Experiments – proton decay studies with ACTAR TPC
from tracks to physics
raw data
corrected
data
calibrated
data
beam line
detector
events selection
corrected
signal
decay
event
ion impl.
event
identified (A,Z) implantations
correlated to decay events

## Slide 77
J. Giovinazzo (LP2iB – CNRS IN2P2 / Univ. Bordeaux)
2025/03 Active Stoppers for Decay Experiments – proton decay studies with ACTAR TPC
from tracks to physics
raw data
corrected
data
calibrated
data
beam line
detector
events selection
corrected
signal
decay
event
ion impl.
event
final distributions for physics
 decay energy (track length)
 decay time curve (decay – impl. time diff.)
experimental
information

## Slide 78
J. Giovinazzo (LP2iB – CNRS IN2P2 / Univ. Bordeaux)
2025/03 Active Stoppers for Decay Experiments – proton decay studies with ACTAR TPC
from tracks to physics
raw data
corrected
data
calibrated
data
beam line
detector
events selection
corrected
signal
decay
event
ion impl.
event
final distributions for physics
 decay energy (track length)
 decay time curve (decay – impl. time diff.)
decay branching ratios
 still need for efficiency corrections !
 simulations
(escape probability, analysis biases,…)
experimental
information
simulation
physics

## Slide 79
J. Giovinazzo (LP2iB – CNRS IN2P2 / Univ. Bordeaux)
2025/03 Active Stoppers for Decay Experiments – proton decay studies with ACTAR TPC
simulations for detection efficiency
tracks fitting procedures control & validation (dispersion, recoil…) – not discussed here
evaluation of missed events fraction
 protons escaping from active volume (E690 & E791)
 protons hidden by implantation signal (E690, short half-life)
 analysis conditions (threshold, cuts,…)

## Slide 80
J. Giovinazzo (LP2iB – CNRS IN2P2 / Univ. Bordeaux)
2025/03 Active Stoppers for Decay Experiments – proton decay studies with ACTAR TPC
simulations for detection efficiency
tracks fitting procedures control & validation (dispersion, recoil…) – not discussed here
evaluation of missed events fraction
 protons escaping from active volume (E690 & E791)
 protons hidden by implantation signal (E690, short half-life)
 analysis conditions (threshold, cuts,…)
simulation processes
• event generator
based on nucleus () implantation distribution
• tracking (Geant4) – emitted particles
gas pressure, geometry
• signal drift and collection
dispersion, gain, fluctuations
• signal processing (from electronics)
shaping, amplification, noise
 many parameters: systematic uncertainties
(+ exp. analysis conditions)
dispersion
response
function
parameters based on
experimental data

## Slide 81
J. Giovinazzo (LP2iB – CNRS IN2P2 / Univ. Bordeaux)
2025/03 Active Stoppers for Decay Experiments – proton decay studies with ACTAR TPC
○ many opportunities for TPC active stoppers for implantation/decay
experiments at fragmentation facilities (RIKEN, … FAIR, FRIB…)
conclusion and perspectives

## Slide 82
J. Giovinazzo (LP2iB – CNRS IN2P2 / Univ. Bordeaux)
2025/03 Active Stoppers for Decay Experiments – proton decay studies with ACTAR TPC
image A. Ortega Moral, PhD thesis 2023
○ many opportunities for TPC active stoppers for implantation/decay
experiments at fragmentation facilities (RIKEN, … FAIR, FRIB…)
○ interesting benefit of associating a gamma detection
for beta-delayed proton decays
 currently considered by collaboration
at Santiago de Compostella
CSi detectors around ACTAR TPC active volume
conclusion and perspectives

## Slide 83
J. Giovinazzo (LP2iB – CNRS IN2P2 / Univ. Bordeaux)
2025/03 Active Stoppers for Decay Experiments – proton decay studies with ACTAR TPC
○ many opportunities for TPC active stoppers for implantation/decay
experiments at fragmentation facilities (RIKEN, … FAIR, FRIB…)
○ interesting benefit of associating a gamma detection
for beta-delayed proton decays
 currently considered by collaboration
at Santiago de Compostella
CSi detectors around ACTAR TPC active volume
○ quite complex data analysis of ACTAR TPC data
 no “standardized” analysis packages (yet ?)
○ analysis tools improvements needed
 efficient tools for events selection & sorting
(machine learning, decision trees, neural networks…)
 tracks fitting procedure (full 3D processing time)
conclusion and perspectives

## Slide 84
J. Giovinazzo (LP2iB – CNRS IN2P2 / Univ. Bordeaux)
2025/03 Active Stoppers for Decay Experiments – proton decay studies with ACTAR TPC
thanks to
the ACTAR TPC collaboration
the E690 collaboration (54mNi/GANIL)
the E791 collaboration (48Ni and others/GANIL)
the LISE3 team
thank you for your attention

## Slide 85
J. Giovinazzo (LP2iB – CNRS IN2P2 / Univ. Bordeaux)
2025/03 Active Stoppers for Decay Experiments – proton decay studies with ACTAR TPC

## Slide 86
J. Giovinazzo (LP2iB – CNRS IN2P2 / Univ. Bordeaux)
2025/03 Active Stoppers for Decay Experiments – proton decay studies with ACTAR TPC
backups

## Slide 87
final result: protons from ACTAR TPC and gammas from RISING
ACTAR TPC exp.: %
RISING campaign: %
Global:
 comparison with theory (shell model)
proton decay half-life:
(B.A. Brown, NuShellX, with GFPX1A and KB3G interactions)
calculations in the fp shell + high ℓ orbitals:
 1 proton in 0h11/2 (ℓ = 5) or 0j13/2 and 0j15/2 (ℓ = 7)
 T1/2 governed by very weak components of the wave functions (10-6)
fairly good agreement for the 2.55 MeV transition to the 7/2− state
not satisfying for the 1.22 MeV transition to the 9/2− state
(mixing with a 2nd 10+ state, less truncated space…)

## Slide 88
54Fe and 54Ni mirror symmetry
complete decay scheme allows for a detailed analysis
 test of isospin non-conserving
terms of the interaction
 constraints on effective isoscalar
and isovector effective charges
from B(E4)

## Slide 89
D. Rudolph et al. Phys. Lett. B (2022)
study of isospin non-conserving terms
different INC terms
different SM
interactions
54Fe and 54Ni mirror symmetry
(D. Rudolph, with code ANTOINE)
very good agreement with experiment can be achieved
for mirror energy differences
but some inconsistencies in the mass region
 not satisfying VCp parametrization
p-orbital occupation numbers very different
for A = 54, A = 56 and A = 58
 deduced effective charges: large discrepancies in B(E4)
for neighbor nuclei 52Mn, 53Fe and 52Fe
D. Rudolph et al. Phys. Lett. B (2022)

## Slide 90
new type of measurement (short lived proton decay)
 3D tracking + decay time
 complete decay pattern of 54mNi with ℓ = 5 and ℓ = 7 proton branches
similar measurement for 53mCo with ℓ = 7 and ℓ = 9
first observed proton radioactivity, 1970
isomer proton radioactivity conclusion
L.G. Sarmiento, T. Roger,
accepted Nature Comm. (2023)

## Slide 91
2-proton radioactivity: theoretical interpretations
• models based on nuclear structure
R-matrix formalism, shell model wave functions, p-p resonance (I. Barker & B.A. Brown)
shell-model embedded in the continuum (SMEC, M. Ploszajczak)
 no dynamics, limited comparison: T1/2(Q2P)
• 3-body model
core+p+p system (L.V. Grigorenko)
 emission dynamics (angular & energy correlations), no intrinsic structure prediction
 good agreement for 45Fe correlation patterns
• recent approaches
- hybrid model (B.A. Brown)
- Gamow Coupled Channels (GCC) (S. Wang & W. Nazarewicz)
3-body
struct.
cont.
3-body
struct.
cont.
3-body
struct.
cont.
angular
& energy
correlations

## Slide 92
the problem of 67Kr half-life
“hybrid” model
shell-model (B.A. Brown)
2-proton amplitudes
for (s2,) p2 and f2 config
“Shell model
corrected half-lives”
A = A(f2) + A(p2)  T1/2(2P)
3-body model (L.V. Grigorenko)
good dynamics
T1/2 for (s2,) p2 and f2 config.
B.A. Brown et al., PRC 2019
calculation experiment(s)
45Fe - ms ms OK
48Ni - ms ms OK
54Zn - ms ms OK
67Kr - ms ms !?
factor
20 to 40 off !!!
B.A. Brown, B. Blank,
J.G, PRC 2019
3-body
struct.
cont.

## Slide 93
the problem of 67Kr half-life
“hybrid” model
shell-model (B.A. Brown)
2-proton amplitudes
for (s2,) p2 and f2 config
“Shell model
corrected half-lives”
A = A(f2) + A(p2)  T1/2(2P)
3-body model (L.V. Grigorenko)
good dynamics
T1/2 for (s2,) p2 and f2 config.
B.A. Brown et al., PRC 2019
calculation experiment(s)
45Fe - ms ms OK
48Ni - ms ms OK
54Zn - ms ms OK
67Kr - ms ms !?
factor
20 to 40 off !!!
2 proposed hypothesis
• transition between direct and sequential 2P emission
(L.V. Grigorenko, 2017)
 different energy sharing
• nuclear deformation
Gamow Coupled Channels formalism (GCC)
(S. Wang & W. Nazarewicz, 2018)
 angular distribution prediction
B.A. Brown, B. Blank,
J.G, PRC 2019
?
L. Grigorenko et al.
PRC 95 (2017) 021601(R)
67Kr
R. Bengtsson & P. Möller (nature, 2007)
3-body
struct.
cont.
3-body
struct.
cont.

## Slide 94
3-body model
not available for 48Ni
extrapolation from 45Fe & 54Zn
pure f2
configuration
GCC…
consistent structure
and dynamics description
good agreement
in the case of 45Fe…
EP1/Q2P
0.5
0
1
energy
sharing
48Ni
67Kr
angular
correlations
spherical
deformed
2P / seq. emission
GANIL
RIKEN
need for new measurements (2018 status)
not up to date
(limited nucleus size)
2021
future

## Slide 95
J. Giovinazzo (LP2iB – CNRS IN2P2 / Univ. Bordeaux)
2025/03 Active Stoppers for Decay Experiments – proton decay studies with ACTAR TPC
charge deposit on a single pad
sampled signal after CSA and shaper… (based on AFTER chip for T2K)
information is “washed out” by AGet shaping
signal distortion: charge pre-amplifier + shaper

## Slide 96
J. Giovinazzo (LP2iB – CNRS IN2P2 / Univ. Bordeaux)
2025/03 Active Stoppers for Decay Experiments – proton decay studies with ACTAR TPC
de-convolution requires each channel response function
use of FFT – need for filtering
shaping
digitisation
analog signal
convolution
de-convolution
signal reconstruction: deconvolution