## Slide 1
Position Sensitive g-ray Detectors from tracking to imaging arrays
Andres Gadea (IFIC-CSIC, Spain)
Maria Doncel (Stockholm University)
GeHP Position Sensitivity and the Tracking array concept development started on mid 90’ in Europe and USA.
Goal was to maximize the solid angle coverage by GeHP in the arrays without loosing P/T performance.
Arrays based on Planar (CUBE, DEGAS) and Coaxial (MARS, AGATA, GRETA) detectors, have been proposed and few are under construction.
Notes: Introduction
Overview of the system
Physics outcomes from this meeting important
define physics case
experimental constraints
range of experiments
key experiments demonstrator/full array
meeting
Key design parameters Before too late
120/180 decision

## Slide 2
European Tracking Arrays based on
Position Sensitive Ge Detectors
Late 90’s Large g-Arrays
EUROBALL
EXOGAM
MINIBALL
Compact g-Arrays optimized Doppler correction, low Mg
AGATA
e ~ 20 % Mg=1
HR g-Spectroscopy Instrumentation for Nuclear Structure
e ~ 10 — 5 %
( Mg=1 - Mg=30)
GAMMASPHERE
e ~ 35 — 24 %
( Mg=1 - Mg=30)
e ~ 17 - 20% (Mg=1) extended sources ~2p  clearance for other detectors
DEGAS
R&D phase

## Slide 3: Position Sensitive Detector for g-rays
4000 V
2000 V
0 V
1 V
0.5 V
0 V
Induced current by the moving charge in the sensing contact  weighting potential Ramo’s Theorem.
Real potential
Weighting potential
Figures courtesy of
M.Ginsz, et al., IPHC Strasbourg
Depth
Radial
Azimuthal
E. Gatti, et al. NIM 193 (82) 651

## Slide 4: Gamma Tracking Array Concept
Pulse Shape Analysis of the recorded waves
Highly segmented
HPGe detectors
Energies, times,
interaction points
(x,y,z,E,t)i
Reconstruction of g-rays from the hits
Synchronized digital electronics to digitize (14 bit, 100 MS/s) and process the 37 signals generated by crystals
Analysis & correlation with other detectors
·
·
·
·
·
·
·
·
g
Event building time-stamped data
Global level
Local level
HARDWARE
SOFTWARE
Readout Raw Data (10 kB/evt/crystal)

## Slide 5
AGATA 4π Performance simulations
CSNSM-Orsay, STFC-Daresbury
Efficiency and P/T Monte Carlo simulations for the
180 Capsules set-up with Tracking
Linear Scaling from known efficiencies
Simulation
For 1 MeV
A. Korichi et al., NIM A 872 (2017) 80
Efficiency %
~1MeV g-rays
Efficiency depends as well on the g-ray multiplicity
Recent Upgraded Simulations by M.Labiche (STFC)
These expectations require the PSA improvements regarding multiple interactions in one segment.

## Slide 6
Tracking:
Imaging:
Reconstruct the path of g rays to improve P/T and background reduction.
Reconstruct the origin of the g ray in the implantation plane for the isomeric decay.
Requirements:
Good energy and position resolution.
High granularity.
Large separation between Ge in the stacks
(increase average distance between interactions)
Requirements:
Good energy and position resolution.
High granularity.
Tracking & imaging concepts
Notes: 6

## Slide 7
Improve the correlation between the implantation and the decay for long-lived isomers
Identify gamma events from the background sources
Suppress the Compton background
Reconstruct the initial energy from Compton escape events and increase the absolute efficiency
Background suppression for tagging of g-rays in isomeric and radioactive decays

## Slide 8
j
“Ideal” Compton Imaging
“Real” Compton Imaging
Ge array configuration including planar detectors?
Coaxial detector
Planar detector
&
Position resolution FWHM ≈ 4-5 mm
Position resolution FWHM ≈ 1-2 mm
A. Khaplanov et al., NIMA 592 (2008) 325
F. Recchia et al., NIMA 604 (2009) 555 P-A Söderström,., et al. NIMA 638 (2011) 96
Thinking on imaging…

## Slide 9
>15% of the area
~4mm
<5% of the area
Realistic g-ray Imaging Capability
Eg = 1.3 MeV
ep
ep ≈ 7 %
ep ≈ 7 %
Wall
Notes: 9

## Slide 10
12 cm
23.5 cm
40 AGATA tapered coaxial HPGe crystals
(9 cm long) + 6 planar HPGe detectors (7*7*2 cm3)
+ Si implantator detector (AIDA)
Idea: AGATA-planar telescope
Composed system: AGATA + planar array takes advantage of the high AGATA efficiency and of the position resolution of planar detectors, about 1-2 mm compared to the 5 mm of AGATA.
Requires R&D
DEGAS (beyond 3rd phase) AGATA type+planar Ge telescope array?

## Slide 11
AGATA at GSI
AGATA + PLANAR’s
In basic capabilities (εp and P/T)
the system is not improved but
we gain imaging capabilities…
Test geometry for DEGAS

## Slide 12
Sum of image matrices for source at two locations with a separation of 60 mm.
S. Moon et al., J. of Instrum. 6 C12048 (2011)
Test measurements
Test without PSA analysis for the AGATA detector
Notes: 12

## Slide 13
Planar position sensitive HPGe detector for combined implantation, beta decay and gamma detection
N. Larson et al., Nucl. Instr. And Meth. A 727 (2013) 59-64
Prototype developed for NSCL beams Ge amorphous contacts (R&D)
Beta decay efficiency ~40% for a single GeHP planar | ~ 90/60% with/without considering neighbouring pixels. Improvements on the tracking (imaging) of g-rays
New Possibility: DSSD-Ge implantation detector
Notes: 13

## Slide 14
35 EUROBALL 3-clusters coupled with 20 AGATA triple clusters + DSSD-Ge planar (8*8*2 cm3) with AIDA?
DEGAS + planar Ge implantation detector
Notes: 14

## Slide 15
New Possibility: DSSD-Ge implantation detector
Optimal solution is to use the Planar DSSD GeHP detector as implanter or in close geometry with the Si implanter AIDA.
Issue: usually Planar DSSD GeHP detectors have one of the contacts made with Li and therefore the detectors can be annealed without destroying completely the contact.
Attempts to use alternative amorphous Ge contacts has not bean successful because these contact are not stable with time.
New detector technology development program started by the AGATA collaboration in the framework of ENSAR2 PSeGe JRA
Also R&D on novel Ge-detector geometries for ultimate position resolution and efficiency included in ENSAR2 PSeGe JRA
HPGe DSSD p-type Lithium segmented contact. Investigation of p-type contacts
Notes: 15

## Slide 16
Towards the AGATA 4p array
Development of HPGe detector production technologies
Developments in contact technology performed in the framework of ENSAR2 (PSeGe) and N3G with PLM techniques at the University of Padova, INFN-LNL and IFIC-Valencia
S. Bertoldo, D. De Salvador, G.L. Maggioni, D. R. Napoli, W. Raniero, A.Gadea
Doping layer
pulse < 100 ns
Doped layer
PULSED LASER MELTING TECHNIQUE
PhD Thesis of Stefano Bertoldo: Uni. Valencia and Uni. Padova.
S. Bertoldo et al., The European Physical Journal A 57 (2021) 177
G. Maggioni et al., The European Physical Journal A 54 (2018) 1
150 nm

## Slide 17
Towards the AGATA 4p array
Some results on HPGe detector production technologies for thick planar detectors
S. Bertoldo, D. De Salvador, G.L. Maggioni, D. R. Napoli, W. Raniero, A.Gadea
PhD Thesis of Stefano Bertoldo: Uni. Valencia and Uni. Padova.
Development of surface treatments, segmentation techniques and passivation

## Slide 18
Towards the AGATA 4p array
Neutron-damage test at CN linear accelerator in INFN-LNL
S. Bertoldo, D. De Salvador, G.L. Maggioni, D. R. Napoli, W. Raniero, A.Gadea
PhD Thesis of Stefano Bertoldo: Uni. Valencia and Uni. Padova.
8.6mm thick p-type 4 segments, Sb junctions

## Slide 19
Achieved Energy resolution
Sb/p-type/Al Square
Side=28mm
Depth=10mm
Guard ring+ central contact
S. Bertoldo, D. De Salvador, G.L. Maggioni, D. R. Napoli, W. Raniero, A.Gadea
PhD Thesis of Stefano Bertoldo:
Uni. Valencia and Uni. Padova.

## Slide 20
Outlook:
The use of tracking detector arrays maximize your solid angle coverage without losing sensitivity. The possibility to incorporate higher position resolution detectors for the g-rays will allow to perform a limited imaging event by event.
Imaging reduces the background, increases P/T and allows higher implantation rates
Detectors should be places as close as possible from the implanter and thus require annealing to repair radiation damage.
New contact technologies are under development that will allow p-type segmented contacts to survive annealing. These developments require new funding that our collaboration is seeking.
Once the contacts are developed we will investigate the effects of radiation damage by implantation of heavy ions as well.