## Slide 1: Generative Surrogate Models for Differentiable Optimization of a Parallel-Plate Avalanche Counter with Optical Readout
María Pereira Martínez, Pietro Vischia, Xabier Cid Vidal
XVII CPAN Days, Valencia
November 20th 2025

## Slide 2
1. Introduction

## Slide 3: Tomography by emission and detection of neutrons for non-destructive tests. High penetration, effective for dense materials like metals and alloys. Metal industry, additive manufacturing, border security…
Neutron tomography
Images from Neutron Insights website

## Slide 4: What do we want to do?
Parallel-plates filled with a high electroluminiscense yield gas (CF4).
Charged particles crossing active volume ionize medium and produce an avalanche.
Electroluminiscense light detected by 4 arrays of small, collimated silicon photomultipliers (SiPMs).
Image from 1808.05882
Optimize the neutron tomography system but… where do we start?
        Optical Parallel-Plate Avalanche Counter

## Slide 5: Optical Parallel Plate Avalanche Counter
Geant4 model of a 1010 cm2 O-PPAC, 33 SiPMs per array
Example of an event triggered by an impining alpha particle:
Image from 1808.05882

## Slide 6: Reconstruction of the position
Reconstructed position () obtained from the number of photons detected in each SiPM
Image from 1808.05882
Weighted average

## Slide 7: Parameters of interest
Collimator Length ():
  Large better resolution, poor statistics
  Small worse resolution, better statistics
Pressure ():
  High pressure higher photon statistics
What is the optimal combination of these parameters?
Image from 1808.05882

## Slide 8
2. Differentiable programming for experiment design

## Slide 9: Differentiable programming for experiment design
Designing experiments is a challenging task.
- Number of parameters can be too high.
- Correlations between parameters can be non-trivial.
- Traditional approaches are computationally costly.
Development of deep learning techniques allows us to explore new approaches

## Slide 10: Differentiable programming for experiment design
1. Model detector modules as differentiable functions of n parameters .
2. Set loss function:
    ()
3. Minimise w.r.t. with automatic differentiation.
Image from Julien Donini - Seminaire LPNHE - 14/02/2022

## Slide 11
3. Automatic optimization of the O-PPAC detector

## Slide 12: Automatic optimization of O-PPAC
(, )
Reconstruction
Geant4 is not differentiable.
Ongoing efforts on making it differentiable (Differentable EM showers in Geant4 - 2405.07944)
Surrogate modelling is a practical workaround.
Approaches:
1. Train a NN to predict the reconstructed position as a function of ().
Geant4
Neural Network
Features
Target
(, )

## Slide 13: Automatic optimization of O-PPAC
(, )
Geant4
Generative model
Features
Target
Geant4 is not differentiable.
Ongoing efforts on making it differentiable (Differentable EM showers in Geant4 - 2405.07944)
Surrogate modelling is a practical workaround.
Approaches:
1. Train a NN to predict the reconstructed position as a function of ().
2. Train a generative model to predict photon distributions from ().

## Slide 14
3.1. Neural Network Surrogate

## Slide 15: 1. NN surrogate
Results published in Particles 2025, 8(1), 26; https://doi.org/10.3390/particles8010026
Solution remarkably stable regardless of initial configuration

## Slide 16
Collimator length result matches the traditional approach: 10.1088/1748-0221/13/10/P10006
1. NN surrogate
Results published in Particles 2025, 8(1), 26; https://doi.org/10.3390/particles8010026

## Slide 17
3.2. Generative surrogate

## Slide 18: 2. Generative Surrogate
Why generative surrogates?
  Can give a more detailed description of detector behaviour.
  Allow us to skip ‘manual’ reconstruction step.
  Freedom to change reconstruction step in the future.
  Trained model will be used later in a bigger pipeline.
Models we are testing:
  GP-WGAN
  -VAE
Hyperparameter tuning:
  TPE algorithm parallelised in gpus.

## Slide 19: 2. Generative Surrogate: Current status and challenges
  -VAE (RMSE = 5.2356)
  GP-WGAN (RMSE = 5.2829)
  Real events

## Slide 20: 2. Generative Surrogate: Current status and challenges
Behaviour is pretty uniform in x, y
but not so uniform in p, L
Proposed solutions:
- Train separate models for different regions.
- Penalize bad behaviour in this region through weights in loss function

## Slide 21: 2. Generative Surrogate: Current status and challenges
- Interesting parameter: error in reconstructed position
- -VAE is better than GP-WGAN but there’s room for improvement.

## Slide 22
Conclusions

## Slide 23: Conclusions
We are applying differentiable programming for the optimization of the O-PPAC detector.
With NN surrogate approach:
  Solution independent of the initial configuration.
  Collimator length result aligns with traditional methods.
With generative surrogate approach:
  GP-WGANs and -VAEs show comparable performance.
  Behaviour is dependent on parameter region.
Next steps
  Improve generative surrogate response throughout the parameter space.
  Try state-of-the-art models:
    Diffusion models
    Normalizing flows
  Build pipeline for the full tomography system.

## Slide 24
Thank you for your attention!
Questions?

## Slide 25
Backup slides

## Slide 26: Vanilla GANs (2014) (https://arxiv.org/abs/1406.2661)
Know problems:
- Training can converge without good results. Loss doesn’t give us information of the quality of the samples
-Inestability: D and G have to be very coordinated through architecture and learning rate. If not, convergence is not guaranteed.
- Mode Collapse: G learns to fool D producing the same event or very few events.
- Overtrained discriminator: if D is very good at classifying events, G cannot learn
Discriminator tries to classify events as real or fake
Generator tries to fool the discriminator into thinking that generated events are real

## Slide 27: Wasserstein GANs (2017) (https://arxiv.org/pdf/1701.07875)
We can use the critic (old discriminator) function as an estimator of the W distance, while the generator tries to minimize it
K-Lipschitz constraint:

## Slide 28: Wasserstein GANs: keys
Train the critic more often than the generator to have a good estimation of WD before updating G
Don’t use batch norm on the critic
Enforce the Lipschitz constraint. Two ways:
    Gradient clipping (not ideal)
    Gradient penalty (https://arxiv.org/pdf/1704.00028)

## Slide 29: β-VAE
L = RMSE(input, output) + β KLD(p(z|x), gaussian)