## Slide 1
Final results of the 239Pu
neutron capture and fission cross-section measurements at n_TOF
Sanchez-Caballero1, V. Alcayne1, J. Andrzejewski2, D. Cano-Ott1, J. García-Pérez1, E. Gónzalez-Romero1, J. Heyse3, T. Martínez1, E. Mendoza1, J. Perkowski2, J. Plaza del Olmo1, A. Plompen3, P. Schillebeeckx3, G. Sibbens3
and the n_TOF collaboration
1CIEMAT, Spain
2University of Lodz, Poland
3JRC-Geel, Belgium

## Slide 2
Contents
Context and Motivation.
239Pu measurement at n_TOF. Experimental setup.
Final results.
Conclusions.

## Slide 3
Context and Motivation
1

## Slide 4
More precise 239Pu capture and fission cross-section data are required for:
Design of advanced nuclear devices (Gen IV reactors).
Optimization of nuclear waste management strategies of current reactors.
Operation of fast and thermal reactors that use MOX fuels.
Nuclear data evaluations for 239Pu(n,g) and (n,f)
Main evaluations for capture cross-sections show significant discrepancies.
Only two high-resolution measurements for 239Pu(n,g) cross-section exist, due to the intrinsic challenge of measuring a fissile sample.
Objective: to reduce the existing uncertainties of for 239Pu(n,γ) and (n,f) cross-sections.
239Pu capture and fission cross-sections are included in the NEA/OECD High Priority Request List.
1. Context and Motivation

## Slide 5
239Pu measurement at n_TOF
2

## Slide 6
2. 239Pu measurement at n_TOF
n_TOF: a neutron Time-Of-Flight facility
A 185 m flight path (10 times larger than in previous 239Pu measurements) enables providing new data with higher energy resolution.
20 GeV/c protons impinging on lead target, produce neutron beam by spallation.
Low pulse repetition rate ~1 Hz; no overlapping pulses!
Broad neutron energy spectrum from meV to GeV.
High intensity neutron flux, ideal for radioactive samples.
n_TOF neutron flux (185 m)

## Slide 7
2.1 Overview of the experiment and samples
The experimental campaign was conducted in the last quarter of 2022, with 2 months of beam time (~5·1018 protons).
The campaign was divided in two different configurations:
The 239Pu targets
The PuO2 (99.90% purity) 10 thin samples (~1 mg each) and the thick sample (~100 mg) were produced, deposited and encapsulated by JRC-Geel+SCK·CEN.
1. FC config.
2. TS config.
- 10 thin Pu samples (<10 mg total mass).
- Use FICH + TAC simultaneously.
- Measure fission and capture (up to 1 keV).
- 1 thick sample (~100 mg).
- Use only TAC.
- Measure capture above 1 keV.

## Slide 8
2.2 Main detectors
Fission Fragment Detector (FFD)
To perform fission tagging with the TAC and to measure fission cross-section.
Housing of 10 parallel targets of PuO2 deposited in 10 µm aluminum backing.
Fast pre-amplifiers.
Filled with Ar+CF4 gas. Efficiency of ~90%.
Total Absorption Calorimeter (TAC)
To measure capture by detecting γ-rays.
Composed of 40 BaF2 crystals.
Fast response, high efficiency and low neutron sensitivity.
Silicon Flux Monitor (SiMon)
Four silicon detectors + LiF foil.
Measure neutron flux based on 6Li(n,α)3H reaction.

## Slide 9
2.3 Experimental setup: mounting
The mounting procedure was similar in both experimental setups.
UPSTREAM VIEW
1. The chamber is placed within the TAC
2. The TAC+FFD assembly is perfectly align with the neutron beam
3. A neutron absorber is placed around the FFD.
Li-doped polyethylene
4. Neutron absorber closed.
5. TAC closed

## Slide 10
Final results
3

## Slide 11
3.0 A glance at the Data Analysis
TAC
Sum energy spectra with the different background components, for the first resonance at 0.3 eV.
MC = Monte Carlo simulation of 239Pu(n,γ).
FFD
Amplitude spectra in the fast fission detector.
FF = Fission Fragment
Vertical line: selected α-FF threshold.
1 FF per >2000 alphas.
E. Mendoza et al. NuDEX: a new nuclear γ-ray cascade generator. EPJ Web of Conferences 239, 17006 (2020)
Access to code (github): https://github.com/UIN-CIEMAT/NuDEX
E. Mendoza et al. Study of photon strength functions of 241Pu and 245Cm from neutron capture measurements. EPJ Web of Conferences 239, 01015 (2020)

## Slide 12
3.1 239Pu fission results
Ratios calculated relative to INDEN
https://www-nds.iaea.org/INDEN/
Integrated fission yield: 100 bins per decade
Fission yield was normalized to an evaluation of the XS integral in the 9-20 eV range.
An overall good agreement with evaluations for 9 orders of magnitude in one-single-measurement!
(from thermal to high energy neutrons)
Our results are also compatible with the 239Pu(n,f) cross section reference (0.15-200 MeV) from the IAEA’s Neutron Data Standards (NDS).
Data | SACS
Derived, this work | 1802±65 (3.6%)
Derived, IAEA standard 20171 | 1798±23 (1.3%)
Mannhart evaluation2 | 1812±25 (1.4%)
Capote et al. evaluation3 | 1826±19 (1.0%)
239Pu(n,f) spectrum-averaged cross section (SACS) in the 252Cf(sf) reference neutron field. Total SACS uncertainties are reported.
Sys. uncertainties of 2-4.5% in the whole range (20 meV to 10 MeV).
1.5% unc. from eval.
n_TOF sys. uncertainties
The new n_TOF 239Pu(n,f) data is being considered for the next evaluation of the NDS.

## Slide 13
3.2 239Pu capture results
The final capture cross section combines the data from both the FC and TS setup.
TS data extends the measurement to higher neutron energies and improves precision in small resonances with too low statistics in FC setup.
FC setup: limited statistics
A clear drop in statistics is observed above a few hundred eV.
<10 mg
TS setup: improved statistics
The larger sample mass provides sufficient statistics to resolve the resonance shapes.
~100 mg

## Slide 14
3.2 239Pu capture results
The results from the FC setup was used to subtract the γ-ray fission background in the TS setup.
Resonance parameters (RPs) were extracted with SAMMY by fitting FC fission, FC capture and TS capture data. The final RPs set combines the results from FC and TS.
10-1
1
10
102
103
104
105
106
107
0.02
eV
239Pu(n,f)
239Pu(n,γ) FC setup
239Pu(n,γ) TS setup
Examples of the SAMMY fit

## Slide 15
3.2 239Pu(n,γ) vs. evaluations
Around the first, large resonance (@0.3 eV), relevant for thermal reactor calculations, the n_TOF data exhibit excellent agreement with ENDF/B-VIII.0, and the largest differences with JEFF-3.3.
10 bins per decade
Larger statistical uncertainties.
Better agreement with E/B-VIII.1, and 3-4% below the other libraries. This deviation is driven by the difference in the fission cross section.
239Pu α-ratio (capture-to-fission)

## Slide 16
3.2 239Pu(n,γ) vs. evaluations
10-100 eV, big discrepancies among evaluations. n_TOF closer to ENDF/B-VIII.1
En>100 eV: n_TOF systematically ~5% above evaluations. Larger diffs. above 1~keV, closer to E/B-VII.1.
2 bins per decade
10 bins per decade

## Slide 17
3.2 239Pu(n,γ) vs. previous data
Scarcity of high-resolution 239Pu(n,γ) cross-section measurements. Two datasets in EXFOR (Gwin 1971, Mosby 2014/2018) mainly used for all evaluations.
@0.3 eV resonance: good compatibility with Gwin 1971 data.
Our capture data exhibit the highest neutron energy resolution among the existing experimental data.
At higher neutron energies, from 1 keV to 10 keV (TS setup), the n_TOF cross section integrals generally stays slightly above Mosby 2018 data.

## Slide 18
Conclusions
4

## Slide 19
4. Conclusions
The data analysis of the 2022 239Pu experimental campaign at n_TOF has been completed, including:
  Data reduction of fission and capture data and extraction of yields.
  SAMMY fit of fission and capture yields, to obtain a final, combined set of resonance parameters.
The measured 239Pu(n,f) cross-section show excellent results in terms of low uncertainties, high energy resolution, and an unprecedented neutron energy coverage from 20 meV to 10 MeV with a single measurement.
The 239Pu capture cross-section measured from 0.1 eV to 10 keV, improving energy resolution of previous datasets with contained systematic uncertainties (2-5% with 5 bins per decade). Significant differences observed with the latest nuclear data libraries, suggesting the revision of some resonances in future evaluations.
Fission paper close to approval for publication.
Capture paper on writing stage.

## Slide 20
This project has received funding from the Euratom research and training programme 2011-2018 under grant agreement No 847595 (ARIEL)
This activity is part of the scientific program approved by the European Commission H2020 Supplying Accurate Nuclear Data for energy and non-energy Applications – SANDA project (WP2, Task 2).
2021-1-RD EUFRAT-GELINA project funding for the stay at JRC-Geel.
Spanish national projects PGC2018-096717-B-C21, PID2021-123100NB-I00 and PDC2021-120828-I00.
Acknowledgments
 | EUROPEAN COMMISSION JOINT RESEARCH CENTRE Directorate G - Nuclear Safety and Security Standards for Nuclear Safety, Security and Safeguards

## Slide 21
THANK YOU!

## Slide 22
Extra slides

## Slide 23
4.1 239Pu(n,f) uncertainties
5 bins per decade

## Slide 24
4.1 239Pu(n,g) uncertainties
DISCLAIMER:
Dummy uncertainties are overestimated in this plot, especially above 100 eV. Final values in the cross-section will be lower.
Valley between resonances
FC setup

## Slide 25
4.1 239Pu(n,g) uncertainties
Target region of the TS setup
TS setup

## Slide 26
4.1 239Pu(n,f) yield compared to evaluations
5 bins per decade
1 bin per decade

## Slide 27
Time coincidences between TAC events and fission chamber (FICH) signals in the energy region close to the 0.3 eV 239Pu resonance.
Coincidence window (-20,+20) ns.
3.3 Coincidence analysis

## Slide 28
Max. En in fission yield
Inspecting the data buffers, we can estimate the width of the gamma flash, thus obtaining the maximum valid neutron energy for the fission yield that we could potentially reach.
Plot taken from file run114394_0_s1.raw.finished. The Tflash has been obtained from Baf2 #18 from the same pulse. TOFD = 185.59 m.
Signal
Fit
Start g-flash (11,196 ns)
End g-flash (~18,000 ns)
3.3 MeV
Signal at 2.2 MeV
Alphas
According to this, we could measure fission without being affected by the gamma-flash up to ~3 MeV.

## Slide 29
Targets description
Number of electronic output from preamplifiers | Target position in the FC chamber | Pu-239 samples | Pu-239 |  | 
Number of electronic output from preamplifiers | Target position in the FC chamber | TP number | Activity [g/cm2] | Mass [g] | Areal density [g/cm2]
6 | 1 | 2020-006-15 | 2.24E+06 | 975 | 310
1 | 2 | 2020-006-02 | 2.22E+06 | 965 | 307
7 | 3 | 2020-006-04 | 2.20E+06 | 959 | 305
2 | 4 | 2020-006-06 | 2.09E+06 | 911 | 290
8 | 5 | 2020-006-14 | 2.81E+05 | 122 | 39
3 | 6 | 2020-006-07 | 1.94E+06 | 844 | 268
9 | 7 | 2020-006-08 | 2.19E+06 | 953 | 303
4 | 8 | 2020-006-10 | 2.11E+06 | 920 | 293
10 | 9 | 2020-006-12 | 2.09E+06 | 912 | 290
5 | 10 | 2020-006-13 | 2.25E+06 | 982 | 312

## Slide 30
Targets description
Target position-2
Target position-1
Target position-4
Target position-3
Target position-6
Target position-5
Target position-8
Target position-7
Target position-10
Target position-9
CLOSER TO NEUTRON SOURCES