## Slide 1: Neutron energy measurements of (α, xn) reactions with MONSTER
José Llanes Gamonoso
jose.llanes@ciemat.es
MONSTER collaboration; MANY collaboration
Unidad de Innovación Nuclear
Departamento de Fisión Nuclear
CIEMAT
Avda. Complutense 40, 28040 Madrid – España

## Slide 2: Table of contents
  Introduction
  Experimental setup
  Data analysis
  Results
  Final remarks

## Slide 3: Table of contents
  Introduction
  Experimental setup
  Data analysis
  Results
  Final remarks

## Slide 4: Motivation
Nuclear data from (α,xn) reactions like yields, cross section, neutron spectra, angular distributions are relevant for:
  Nuclear reactors and fuel cycles
  Experiments in basic nuclear physics:
    Dark matter
    Neutrinos
  Medical applications
The available experimental data are outdated, incomplete, or have large uncertainties New measurements (MANY collaboration)
D. Cano-Ott et al., J. Phys. G: Nucl. Part. Phys., (2025)
S.S. Westerdale et al., Summary report of the Technical Meeting, 8-12 Nov 2021 (virtual event)

## Slide 5: Measurement of Alpha Neutron Yields and Spectra (MANY)
Two Spanish facilities
Three Spanish detectors
miniBELEN
LaBr3 array
miniBELEN
GARY

## Slide 6: Measurement of neutron spectra in (α,xn) reactions
neutron detectors
(liquid/plastic scintillators)
TOF spectrometer:
Requires a pulsed α-beam.
Information for the eff correction εn(En)
Measurements at different angles allows the study of angular distribution
Low efficiency (~ 1%)
Neutron/gamma discrimination and correlation with γ-rays
MONSTER
Our experimental setup
Within MANY collaboration, we are interested in:
Neutron yields and cross sections miniBELEN and GARY
Neutron spectra and angular distribution MONSTER

## Slide 7: Table of contents
  Introduction
  Experimental setup
  Data analysis
  Results
  Final remarks

## Slide 8: Experimental setup
HiSPANoS facility at the Centro Nacional de Aceleradores (CNA), Seville:
  3 MV tandem accelerator: to produce the α particles (between 5.5 and 8.5 MeV) (1)
Five cells of MONSTER between and (2)
Four LaBr3 detectors (3) and a HPGe detector (4)
  (3) and (4) dedicated to γ measurements γ/n correlated events
27Al target: d = 2.5 cm, thickness = 150 μm, purity = 99.9 %
A.R. Garcia et al., Journal of Instrumentation, 7, (2012) C05012
T. Martínez et al., Nucl. Data Sheets, 120, (2014) 78-80

## Slide 9: 27Al(α,n)30P reaction
IAEA suggests the use of this reaction as a benchmark
Aluminum is a very common element in structural materials
There is available data for 27Al(α,n)30P reaction
The reaction mechanism is well-known:
  β+ emission of 30P allows the yield measurement
G.J.H. Jacobs & Liskien, Annals of Nuclear Energy, 10, (1983) 541-552
A. Junghans et al., INDC International Nuclear Data Committee (IAEA), (2023)

## Slide 10: MONSTER spectrometer
Cells are filled with a scintillating liquid (BC501A or EJ301)
Good time resolution (< 1 ns)
These detectors have a good neutron/γ-ray discrimination capability Pulse Shape Discrimination (PSD)
n
t (CFD)

## Slide 11: Table of contents
  Introduction
  Experimental setup
  Data analysis
  Results
  Final remarks

## Slide 12: Inverse problem
Measured neutron TOF spectrum
Response matrix
Neutron energy distribution
Measured neutron TOF spectrum Neutron selection over raw data
Response matrix Accurate Monte Carlo simulations with Geant4
Neutron energy distribution Solving the inverse problem by an unfolding algorithm
S. Agostinelli et al., Nucl. Inst. and Meth. A, 506, (2003) 250-303

## Slide 13: Neutron Selection
Raw TOF spectra
Difficult to see the neutrons due to high contribution -peak and uncorrelated background
Necessity of a neutron cut
MeV
Neutron cut
-peak
neutron structure
uncorrelated background

## Slide 14: Neutron Selection
Raw TOF spectra
MeV
No γ contribution Neutron TOF obtained
Neutron structures are now highlighted
Neutron cut

## Slide 15: Response matrix
Construction of the response matrix :
  Cover the whole neutron energy range
  Provide TOF response for each considered neutron energy
  The energy bin width is according to MONSTER resolution: ns
0º MONSTER cell
Neutron/(Source Particle)
TOF (ns)

## Slide 16: Response matrix and unfolding algorithm
Iterative Bayesian method :
  Bayes formula
This methodology is validated with simulations (1) and real experiments (2)
(1) A. Pérez de Rada Fiol et al., Rad. Phys. Chem. 226 (2025) 112243
(2) A. Pérez de Rada Fiol et al., Phys. Rev. C, 111, (2025), 044312
Causes
Effects
independent causes
effects
response matrix
initial guess
G. D'Agostini, Nucl. Instrum. and Methods A, 362 (1995) 487-498
Neutron/(Source Particle)
TOF (ns)
MeV, 0º MONSTER cell

## Slide 17: Table of contents
  Introduction
  Experimental setup
  Data analysis
  Results
  Final remarks

## Slide 18: Neutron energy distributions: comparison with previous data (MeV)
G.J.H. Jacobs & Liskien, Annals of Nuclear Energy, 10, (1983) 541-552
Good agreement with previous data (within 10 %)

## Slide 19: Angular distribution (MeV)
Fit function:
Reaction kinematics:
  Higher neutron yield/integral with decreasing angle Maximum in the direction of the α beam line
0 °
R. M. Sealock, Nuc. Phys. A, 357, (1980) 279-292

## Slide 20: Neutron energy distributions: all energies (angle = 0º)
Higher neutron energy and yield with higher
Maximum neutron energy corresponds with the minimun TOF per each

## Slide 21: Neutron energy distributions: structures (angle = 0º)
Different structures due to the population of different excited states of 30P for different

## Slide 22: Table of contents
  Introduction
  Experimental setup
  Data analysis
  Results
  Final remarks

## Slide 23: Final remarks
First measurements of the (α,xn) reaction on a thick 27Al target with MONSTER at the Centro Nacional de Aceleradores (CNA)
  α energies from 5.5 MeV to 8.5 MeV 6 new energy spectra measured!
Clean TOF spectra obtained after neutron selection
Neutron spectra have been obtained and compared to existing data
Study of the angular distribution started
Uncertainty analysis of the results is ongoing
Future work:
  Repeat the experiment at CMAM
  Study other (α,xn) reactions with other isotope targets, e.g., 9Be

## Slide 24: Thanks for your attention
MANY collaborators
V. Alcayne6, A. Algora2, O. Alonso-Sañudo3, G. Auñón7,8, D. Bachiller-Perea6, J. Balibrea-Correa2, J. Benito3, M. J. G. Borge5,4, J. A. Briz3, F. Calviño1, D. Cano-Ott6, G. Cortés1, A. De Blas1, C. Domingo-Pardo2, A. Espinosa3, B. Fernández7,8, L. M. Fraile3, G. Garcia4, R. García1, V. García Tavora4, J Gómez-Camacho7,8, E. M. González-Romero6, C. Guerrero7,8, A. Illana3, J. Lerendegui-Marco2, J. Llanes-Gamonoso6, M. Llanos3, T. Martínez6, V. Martínez-Nouvilas3, E. Mendoza6, N. Mont-Geli1, J. R. Murias3, E. Nácher2, A. Nerio Aguirre5, V. V. O. Onecha3, S. E. A. Orrigo2, M. Pallàs1, A. Perea5, A. Pérez de Rada Fiol6, V. Pesudo6, J. Plaza6, J. M. Quesada7, A. Sanchez-Caballero6, V. Sánchez-Tembleque3, R. Santorelli6, J. L. Tain2, A. Tarifeño-Saldivia2, O. Tengblad5, J. M. Udías3, D. Villamarín6, S. Viñals4
1Institut de Tècniques Energètiques (INTE), Universitat Politècnica de Catalunya (UPC), E-08028, Barcelona, Spain
2Instituto de Física Corpuscular (IFIC), CSIC – Univ. Valencia (UV), E-46071, Valencia, Spain
3Grupo de Física Nuclear (GFN) and IPARCOS, Universidad Complutense de Madrid (UCM), E-28040, Madrid, Spain
4Centro de Micro-Análisis de Materiales (CMAM), Universidad Autónoma de Madrid (UAM), E-28049, Madrid, Spain
5Instituto de Estructura de la Materia (IEM), CSIC, E-28006 Madrid, Spain
6Centro de Investigaciones Energéticas, Medioambientales y Tecnológicas (CIEMAT), E-28040, Madrid, Spain
7Departamento de Física Atómica, Molecular y Nuclear, Universidad de Sevilla (US), E-41012 Sevilla, Spain
8Centro Nacional de Aceleradores (CNA) (Universidad de Sevilla (US) - Junta de Andalucía - CSIC), E-41092, Sevilla, Spain
José Llanes Gamonoso
jose.llanes@ciemat.es
Acknowledgements
This work was supported in part by project PID2021-123100NB-I00 funded by MCIN/AEI/10.13039/501100011033/FEDER, UE and in part by the European Union’s HORIZON-EUROPE Research and Innovation Programme under grant agreement No. 101164596 (APRENDE, addressing priorities of evaluated nuclear data in Europe. WP2.). The support by the ENRESA-CIEMAT agreement 2023-2026 "Tecnologias disponibles para la transmutacion de radionucleidos de vida larga" is also acknowledged.