## Slide 1
PROTOTWIN:
PET Imaging and AI to Improve Proton Therapy
Pablo Cabrales Miró-Granada (pcabrale@ucm.es)

## Slide 2
How can PET and AI improve proton therapy?
Providing clinicians crucial information to:
Part 1: Verify the treatment
Part 2: Adapt the treatment
Enabling more personalized and effective patient treatment
Physical information (dose) from static PET
Biological information (tumor status) from dynamic PET
min-1
Washout
Rate
?
Why now?
But let’s start with an introduction…
Greater sensitivity (e.g. time-of-flight) and AI enhance PET
Notes: With better PET (improved time-of-flight) and AI you can improve PET beyond what was possible; PET had been studied for proton therapy in the past but it is still not widely used

## Slide 3
Proton therapy targets tumors more precisely than photon-based radiotherapy
X-rays
Protons deliver most of their energy within the tumor (Bragg Peak🎯)
Credit: IBA
Photon-based radiotherapy
Proton therapy
Notes: Delivers most of their energy within the tumor, as opposed to photons, due to the interaction between protons and the patients bodies

## Slide 4
Proton therapy keeps improving and growing
Advances in treatment delivery, adaptation, optimization [Mohan, Prec. Radiat. Oncol., 2022]
Source: ptcog.site
Cumulative evidence: clinical trials for head-and-neck, brain, pediatric…
Proton facility at Clínica Universidad de Navarra
Notes: - Proton therapy, has been growing in terms of numbers of patients treated (>500k) and number of clinical facilities
- Since the five year survival rate for cancer is at approximately 70%, a priority is minimizing secondary effect, e.g. cognitive decline in pediatric pediatric CNS patients or xerostomía in head and neck patients

## Slide 5
Part 1 of 2:
PROTOTWIN-PET:
A Deep Learning and GPU-Based Workflow
for Dose Verification in Proton Therapy with PET
Pablo Cabrales1,2, Víctor V. Onecha3, David G. Izquierdo3, José Manuel Udías1,2,
Luis Mario Fraile1,2, and Joaquín L. Herraiz1,2
📜 Published in IEEE TRPMS (2025)
(1) (2) (3) (4)

## Slide 6
Treatment uncertainties limit proton advantage
Protons can be very precise, but the real world is messy: treatments are sensitive to uncertainties
Patient setup
Organ motion
Tissue properties
Photons
Protons
Organ-at-risk
Dose
Adapted from:
Knopf, Lomax,
Phys. Med. Biol.,
2013
Dose
Tumor
Irradiation margins are introduced to ensure tumor coverage, damaging organs-at-risk
Organ-at-risk
Tumor
Tumor
Irradiation margins
Organ-at-risk
Notes: - treatment are very sensitive to uncertainties due to the highly localized dose delivery make the
Margins are introduced in the planning target volumen to ensure that there is no cancer recurrence

## Slide 7
Treatment verification can improve efficacy
Secondary emissions like acoustic waves, prompt gamma photons, positron-emitting isotopes 11C, 13N, 38K → Positron Emission Tomography (PET)
p+
γ
Credit: LMU and Jens Maus
γ
Detecting deviations enables adaptation and reducing margins
Organ-at-risk
Tumor
Irradiation margins
How can we know if we have hit (or missed)
the target? Treatment verification
Notes: Since protons stop inside the patient, dose delivery verification relis on secondary emissions
Positron Emission Tomography has been studied the most and the approach I consider in my work
We need to know where the radiation, which is usually called radiation dose, or dose is delivered to know if treatment has gone as planned or if we have damaged healthy tissue and underdosed the tumor. Since radiation therapy treatments are spaced across around 30 sessions, dose delivery errors in one session can be corrected in following sessions

## Slide 8
Produced Positron Emitters
Estimated Radiation Dose
Protons
PET
Deep Learning (DL)
Current DL approaches [Peng et al., IEEE TRPMS 2023]:
Unrealistic training data (missing PET simulation, clinical uncertainties) and CPU-based tools (slow)
Lack end-to-end workflows
kBq/cc
Gy
Challenging! Different processes, noisy PET images (low counts, washout)
PET-based verification requires fast and accurate end-to-end workflows
Notes: We can compare obtained and expected PET distributions, but it is not as insightful
the conversion from PET to dose is not straightforward because, while dose depositions are related to interactions between protons and the atomic electrons, destroying the cell dna, PET activations correspond to nuclear interactions, and thus take place at different energies and are not directly correlated. unrealistic datasets do not consider effects that will appear in the clinical practice and that our model needs to be shown in training so that it can work in the clinical practice
Made key advancements

## Slide 9
github.com/pcabrales/prototwin-pet
doi.org/10.1109/TRPMS.2025.3531536
Proposed Workflow for Improved Verification
Notes: Treatment deviations reflect how treatment might go wrong

## Slide 10
github.com/pcabrales/prototwin-pet
doi.org/10.1109/TRPMS.2025.3531536
Proposed Workflow for Improved Verification
Notes: Treatment deviations reflect how treatment might go wrong

## Slide 11
Realistic dataset is generated for training
Physical parameters (tissue density and ionization energy, up to 10%)
Model training with >100 PET-dose pairs
Details at github.com/pcabrales/prototwin-pet
Each 3D PET-Dose pair reflects a realistic treatment deviation
Patient setup
Notes: Displacements in the directions parallel to the couch

## Slide 12
github.com/pcabrales/prototwin-pet
doi.org/10.1109/TRPMS.2025.3531536
Proposed Workflow for Improved Dose Verification

## Slide 13
github.com/pcabrales/prototwin-pet
doi.org/10.1109/TRPMS.2025.3531536
Proposed Workflow for Improved Dose Verification

## Slide 14
Model is trained to simultaneously estimate dose and setup errors from the PET image
Notes: CT is provided for anatomical context Unet-like models extract high and low level features; attention captures relationships between distant parts of the image
Extra:
DPB starts at penultimate encoder layer because the spatial representation was potentially overly compressed at the bottleneck and information was lost before that
Lambda is a hyperparameter that was tuned experimentally

## Slide 15
github.com/pcabrales/prototwin-pet
doi.org/10.1109/TRPMS.2025.3531536
Enables online
Proposed Workflow for Improved Dose Verification
and offline
Dose Verification from PET Scan
Notes: For anyone that want to take a look at it and maybe try it out

## Slide 16
150 training PET-Dose pairs for oropharyngeal cancer patient (2.2 Gy, 2 fields)
Generated in < 20 hours, model trained in 3 hours (RTX 4080 GPU)
Offline verification: 10 minutes post-irradiation,
30-minute Siemens Biograph Vision PET scan
Workflow is validated in silico
Input: PET and CT
Output: Dose
Gy
kBq/cc
Notes: Let’s see how this would work for a patient: they have a tumor …, the treatment might have gone wrong due to unexpected patient motion
Offline only requires a convenional PET

## Slide 17
30 ms
Previous works: ~1.5
Trained model accurately estimates delivered dose for clinically significant deviations
PROTO-
TWIN-
PET
Test Case
[Ma et al., Med. Phys. (2020),
Rahman et al., Phys. Med. Biol. (2022)]
Reference: Planned vs Actual
Actual vs Estimated
PROTO-
TWIN-
PET
Notes: It’s a test sample
- en diferentes métricas mejora bastante respecto al caso en que no se estima la deposicion de dosis y se considera que es igual a la planeada
Without prototwin-pet, we would not be aware of the difference between the planned and actual delivered dose; with it, we can correct it in following sessions

## Slide 18
Across 50 test cases (MRE < 2%):
|Δxestimated - Δxactual| = 0.04 ± 0.07 mm
|Δyestimated - Δyactual| = 0.03 ± 0.05 mm
|Δθestimated - Δθactual| = 0.05 ± 0.07 º
Trained model detects setup errors with submillimetric accuracy (in silico)
Setup Deviation Error (º or mm)
Notes: Submillimetric precision in silico, in our simulation, in reality we would have to see how accurate we can be

## Slide 19
Ablation Study: How does training models with unrealistic PET inputs impact performance?
Notes: One may wonder: this workflow is complicated, but how necessary is including the steps to make the PET image realistic

## Slide 20
Gaussian blurring
instead
Ablation Study: How does training models with unrealistic PET inputs impact performance?

## Slide 21
C11
Capillary
Blood Cells
Ablation Study: How does training models with unrealistic PET inputs impact performance?

## Slide 22
Ablation Study: How does training models with unrealistic PET inputs impact performance?

## Slide 23
Ablation Study: How does training models with unrealistic PET inputs impact performance?

## Slide 24
PET simulation and washout are critical for reliable dose estimation
Ablation Study: training models with unrealistic PET inputs significantly degrades performance
Notes: The performance downgrade is most significant for models trained without the realistic PET acquisition simulation and washout effects. In contrast, the impact is less severe when only 11C activations are considered and the positron range is omitted. This outcome is expected since positrons emitted from activated isotopes have relatively low energies, and 11C is the most uniformly and abundantly contributing isotope

## Slide 25
Potential to shrink margins and minimize healthy tissue damage
Conclusions: PROTOTWIN-PET accurately verifies dose delivery in milliseconds
Limitations: uncertainty remains in interaction cross-sections, PET-CT registration, or biological washout parameters
Validation in real scenarios is essential: Clínica Universidad de Navarra (CUN) and Massachusetts General Hospital (MGH) …

## Slide 26
Experiments at CUN aim to validate simulations and AI models
July 2025
PET
Proton
Therapy
Thanks to Dr. Diego Azcona, Dr. Ana García Sanz, Dr. Edgar Guillén, Lucía Meijón
Simulated PET
Real PET
Activity (A.U.)

## Slide 27
Real PET
Before: “Simulated” PET
After: Simulated PET
>70 post-proton therapy PET scans (2014 to 2020)
Analysis of MGH data reveals the importance of PET simulation
Thanks to Dr. Helen A. Shih, Dr. Kira Grogg, Dr. Xuping Zhu
* Red line = beam direction
Notes: Data infrautilized
Massachusetts general hospital

## Slide 28
Part 2 of 2:
Mapping Intratumoral Heterogeneity Through
PET-Derived Washout After Proton Therapy
Pablo Cabrales1,2, David G. Izquierdo3, Víctor V. Onecha3, Mailyn Pérez-Liva,
José Manuel Udías1,2, Luis Mario Fraile1,2, and Joaquín L. Herraiz1,2
📜 Preprint in arXiv (2025)
(1) (2) (3) (4)
Notes: Can we get any more information: Dynamic PET to extract biological insight

## Slide 29
Dynamic, complex, tissue-dependent processes displacing proton-produced positron emitters and reducing PET image SNR
λB: Biological Washout Rate
Dynamic post-proton therapy
PET at MGH
kBq/cc
Biological washout:
problem or opportunity?
Credit: Mizuno et al 2003 Phys. Med. Biol.
Notes: - like perfusion and cellular metabolism
- refer back to the first part (treatment verification)

## Slide 30
Perfused
Hypoxic
* Toramatsu et al., Phys Med Biol, 2022
Fiedler et al., Acta Oncologica 2010
Washout Rate
Can accurate washout mapping at intratumoral scales provide clinically relevant information?
Washout can be estimated with dynamic PET post-treatment to correct it and inform tumoral status (vascularity, tissue response*)
Biological washout:
problem or opportunity?
But low SNR limits washout estimation (approximate, tumor-wide)
Notes: Higher washout rates mean that the tumor is more perfused
with DCE-MRI and histological analysis

## Slide 31
Intratumoral heterogeneity relates to tumor progression and survival: surrogate marker to improve risk stratification, tumor assessment, and personalized treatment [Zhao et al., Eur J Nucl Med Mol Imaging, 2022]
Heterogeneous tumors respond worse
Beaton et al., Br J Cancer, 2019
Currently: tracers (>2000$*), + radiation, may not reach regions
*www.martinos.org/core-services-fee-chart
Notes: (e.g. finding aggressive regions)
Extra:
Normal-tissue exposure from a full external-beam radiotherapy course (beam leakage/scatter): 300 mSv
Additional radiation due to PET imaging: ~5 mSv

## Slide 32
Can we accurately map washout to reveal intratumoral heterogeneity non-invasively?
min-1
Washout Rate
Cluster 1
Cluster 2
Cluster 3
Cluster 4
?
Challenge: direct estimation from dynamic PET after proton therapy is noisy and blurred due to low counts
Notes: (e.g. finding aggressive regions)
To overcome the low SNR, we develop a deep learning workflow

## Slide 33
(C) Proton
Therapy
Simulation
(D) Introducing
Tumor Heterogeneities
(A) Patient Selection
(E) PET acquisition
simulation
(F) Dynamic PET
reconstruction
(G) Voxel-wise
activity fit
…
A
t (min)
λB : Biological Washout Rate
(H) Fit Correction
(I) Direct Estimation
min-1
min-1
*[Kendall et al., NeurIPS Proceedings, 2017; Seitzer et al., arXiv:2203.09168, 2022]
Washout Rate Map (λB)
with Uncertainty*
Ground Truths
(75 digital twins)
Vascularized
Necrotic
min-1
kBq/cc
Uncorrected
λB
Ao
15 min delay,
30 min scan
Head and neck
cancer
https://github.com/pcabrales/ppw
Proposed Workflow for Improving Washout Mapping and Revealing Heterogeneity
Dataset Generation
Model Training
(B) Treatment Planning
Washout Mapping after Proton Therapy from PET Scan
15 min delay
~80% is 11C
Notes: - WE WANT TO TURN THIS PROBLEM OF WASHOUT INTO AN OPPORTUNITY FOR BIOLOGICAL TUMOR ASSESSMENT. This is how we do it
For each patient’s digital twin we introduce heterogeneities inside the tumor, áreas with different washout rates
At imaging times, activity Will be governed by the slower components of 11C washout. We are focusing on the washout rate but we have developed another way to include the faster components, look at the preprint
- * Uncertainty = Aleatoric (intrinsic noise; learned β−NLL loss) +
Epistemic (model stability; Monte Carlo Dropout)

## Slide 34
Trained models help reveal heterogeneity
High uncertainty aligns with higher errors ✓
Notes: Let’s see the tumors of some patients….; how would it help the patient/oncologist?
Uncorrected maps suffer from spillover effects
Uncertainty estimates align with regions of higher error (also made a sparsification error plot)
You activate regions that you would not reach with blood flow (conventional radiotracer)
Extra:
(Epistemic uncertainty was low compared to aleatoric, reflecting that most
Techniques which can be applied to Dynamic low-dose PET

## Slide 35
Models generalize across
Anatomical regions
PET acquisition timings
Trained models enable separating intratumoral regions larger than 5 mL
[Toramatsu et al., Phys Med Biol, 2022]
Trained
Models
***
***
***
***
***
***
***
***
***
***
Trained models improve washout maps
PET scanners
Notes: As expected, higher error for smaller regions
- Differences between hypoxic and control and perfused and control regions are close to 0.01

## Slide 36
Conclusions: non-invasive, robust washout estimation and heterogeneity assessment
Potentially enabling:
Tumor response evaluation and risk stratification
Treatment adaptation (e.g. dose painting)
Improved PET-based treatment verification [Cabrales et al., IEEE TRPMS, 2025]
Validation in real patients is essential: Massachusetts General Hospital (MGH) and Clínica Universidad de Navarra (CUN)…
min-1
Washout Rate
Notes: Non-invasive because it leverages intrinsic radioactivity

## Slide 37
>70 post-proton therapy PET scans (2014 to 2020)
Analyzing MGH study data
In progress: assessing if regions observed with PET match those from other modalities after applying our framework
Thanks to Dr. Helen A. Shih, Dr. Kira Grogg, Dr. Xuping Zhu
PRELIMINARY
Notes: Data infrautilized
MGH, USA
Introducing our framework to enhance separation of washout in different tissues
-e.g. are hypoxic regions also hypoxic in the obtained washout maps?
Count rate: 10k/second
Randoms rate: 0.05%

## Slide 38
Acknowledgements
Supported by Spanish MCIN/AEI/10.13039/501100011033 and the European Union NextGenerationEU/PRTR under grants TED2021-130592B-I00 PROTOTWIN, PID2021-126998OB-I00 FASCINA, and PDC2022-133057-I00 3PET; by Comunidad de Madrid (Spain) under projects ASAP-CM P2022/BMD-7434 and TAU-CM PR47/21 (PRTR), and by Grupo de Física Nuclear (910059) at Universidad Complutense de Madrid. Additionally, Pablo Cabrales acknowledges support from the Complutense University Predoctoral Fellowship (CT15-23), funded by the Universidad Complutense de Madrid and Banco Santander, as well as from the Ayuda para estancias breves fellowship (EB33/24), funded by the Universidad Complutense de Madrid.

## Slide 39
Pablo Cabrales Miró-Granada
pcabrale@ucm.es
Questions? Thank you
Published in
IEEE TRPMS, 2025
Code is available on GitHub
github.com/pcabrales/ppw

## Slide 40: Additional material

## Slide 41
Pablo Cabrales Miró-Granada
Grupo de Física Nuclear @ UCM
pcabrale@ucm.es
Code is available on GitHub
github.com/pcabrales/ppw
Questions? Thank you

## Slide 42
Pablo Cabrales Miró-Granada
Grupo de Física Nuclear @ UCM
pcabrale@ucm.es
Code is available on GitHub
github.com/pcabrales/ppw
Questions? Thank you
Washout Rate (min-1)
This work:

## Slide 43
Role of the Vision Transformer: nnUnet vs nnFormer
Vision transformers may improve results by capturing correlated effects through the image
nnFormer also outperformed (and is lighter) than UXNet, SwinUNETR, TransBTS, attention UNet, vanilla UNet

## Slide 44
Role of the Vision Transformer: nnUnet vs nnFormer
Vision transformer role is greater in nnFormer than other CNN + transformer architectures, may indicate that it is the differential factor for our task (image translation: PET → Dose) where long-term spatial correlations are significant
(For biomedical image segmentation)
[Wald et al., 2025
arXiv:2503.01835]
Notes: Question may be: why is nnFormer outperforming other models?

## Slide 45
Protons leave correlated effect through image
  CNN + Vision Transformers (nnFormer) better than
pure CNN (nnUnet)?
  Compared architectures (detailed later)
Images are 3D and large (128⨯96x128) for GPU
Batch size = 1, accumulated gradients (4 batches) for stability
AdamW (learning rate = 0.001) and cosine annealing scheduling
600 epochs with early stopping (patience = 50 epochs)
Patient position is important: no spatial (e.g. rotation) data augmentation
Deep Learning Training

## Slide 46
Trustworthiness in medical AI is key: know what the model doesn’t know
Aleatoric uncertainty
  Reflects intrinsic noise in PET data
  Estimated by the model
  Output A =
Epistemic uncertainty
  Reflects lack of model knowledge and stability
  Std dev of 20 MC dropout passes with 20% dropout rate
[Kendall et al., NeurIPS Proceedings, 2017;
Seitzer et al., arXiv:2203.09168, 2022]
Model Architecture and Uncertainty Estimation

## Slide 47
- Post-proton therapy PET scans conducted from 2014 to 2020 (>30 patients, >70 scans, MRIs)
MGH study data analysis
- Analysis in progress: already seeing the importance of PET simulation
Thanks to Dr. Helen A. Shih, Dr. Kira Grogg, Dr. Xuping Zhu
Notes: Data infrautilized

## Slide 48
Pablo Cabrales Miró-Granada
Grupo de Física Nuclear @ UCM
pcabrale@ucm.es
Code is available on GitHub
github.com/pcabrales/ppw
Questions? Thank you
Washout Rate (min-1)
This work: