## Slide 1
Medical applications with laser accelerators
Jose Benlliure
Instituto de Física Corpuscular (CSIC – Univ. Valencia), Spain
30 October 2025, Valencia, Spain
Jornadas PROMESA
Notes: 1
1

## Slide 2
José Benlliure
The societal impact of particle accelerators
2
Particle accelerators have evolved from a research tool to a technology with a major societal impact.
Jornada PROMESA, 30 de October de 2025

## Slide 3
José Benlliure
Some numbers
There are about 35,000 accelerators in operation worldwide.
34% medical applications (~10000 e-, ~ 1400 protons, ~14 ions).
34% ion implantation (~12000)
28% industrial sterilisation (~10000 e-)
6% fundamental research (~200 ).
The market for accelerators dedicated to medical and industrial applications exceeds $5000M per year and is growing at more than 8% annually.
Some 250 accelerators are in operation in Spain.
231 electron accelerators for radiotherapy.
17 cyclotrons for the production of PET radioisotopes.
2 cyclotrons for proton therapy (11 more soon).
3 accelerators for fundamental and applied research (CNA-Sevilla, CMAM-
Madrid y ALBA-Barcelona).
The societal impact of particle accelerators
3
Jornada PROMESA, 30 de October de 2025

## Slide 4
RF particle acceleration technology
José Benlliure
Mature technology facing some challenges
Accelerator technology made great strides during the 20th century.
1931
2010
10 cm
4.5 Km
MeV
TeV
But in the 21st century it has encountered two main limitations:
Difficult to increase the acceleration gradient with RF technology ~107 V/m.
Energy can only be increased with length (future circular collider e-e+ 100 TeV ~100 km)
The cost of accelerators increases with the physical space they occupy.
Accelerator shielding (concrete) costs more than the accelerator itself.
4
Jornada PROMESA, 30 de October de 2025

## Slide 5
A new technology for particle acceleration
2004
2018
Laser-plasma accelerators rely on the Chirped Pulse Amplification invented by Mourou and Strickland.
José Benlliure
5
Jornada PROMESA, 30 de October de 2025

## Slide 6
Laser-plasma acceleration in a nutshell
Ultra-intense and ultra-short laser pulses with power densities above 1018 W/cm2 , traversing an electron plasma, create a charge separation which can build up to a charge-density wave (wakefield) of the order of TV/m. Electrons entering this wakefield are accelerated to relativistic energies.
José Benlliure
6
A section of RF cavity
A plasma wave
Electron acceleration
Jornada PROMESA, 30 de October de 2025
Notes: 6
6

## Slide 7
Laser-plasma acceleration in a nutshell
Ultra-intense and ultra-short laser pulses with power densities above 1018 W/cm2 , traversing an electron plasma, create a charge separation which can build up to a charge-density wave (wakefield) of the order of TV/m. Electrons entering this wakefield are accelerated to relativistic energies.
José Benlliure
7
Electron acceleration
The cloud of accelerated electrons leaves the target material, ionizing its rear surface and forming a charge-separation field, also of the order of TV/m. Such fields accelerate the ions, normal to the surface.
Ion acceleration
Jornada PROMESA, 30 de October de 2025
Notes: 7
7

## Slide 8
Laser-plasma acceleration in a nutshell
José Benlliure
8
Pros
Cons
IR beam
~10 mm
~20 cm3
Extremely high acceleration gradients (~TV/m).
Compactness and portability.
Lower cost (laser and shielding).
Flexibility in particle species.
Ultra-short ion bunches.
High beam currents (~1012 ions/pulse).
Energy spread and poor beam quality.
Limited reproducibility.
Relatively low maximum energies (~150 MeV).
Target replenishment and debris.
Low repetition rate (< 100 Hz).
Jornada PROMESA, 30 de October de 2025
Notes: 8
8

## Slide 9
Medical applications with laser-accelerated ions
José Benlliure
9
Michael Seimetz
Radioisotope production
UHDR (Flash) radiobiology
Phase-contrast X-ray imaging
LPA could be the enabling technology to produce in-house on-demand doses of PET probes of interest at low cost, in an automated, user-friendly device (short-lived, i.e. 11C).
Laser accelerators naturally produce ultra-short particle pulses that meet the requirements of flash radio-therapy. Moreover, they do not require a gantry.
For materials with low absorption (e.g. biological matter) the phase shift can gives orders of magnitude stronger contrast than absorption.
Laser-induced X-ray sources fulfill the conditions for phase-contrast imaging: small size sources (~10 mm) and high fluxes.
Jornada PROMESA, 30 de October de 2025
Notes: 9
9

## Slide 10
José Benlliure
High repetition rate targets
The target material used to accelerate the ions (~ 1 mm) has to be replaced and positioned with an accuracy better than 10 mm every 100 ms (10 Hz).
7
1 hour operation.
Continuous
operation.
~10 mm
Key technologies in laser acceleration at IFIC
15 minutes operation.
New diagnostics
The detection of laser-accelerated particles faces two major challenges:
Huge particle fluxes (~1012 ions in t < 1 ps).
Large electromagnetic noise.
Integral measurements with quasi-optical detectors:
Scintillating plastics or gases.
Photo-sensors decoupled with optical fibers.
Plastic scintillators
Scintillating
fibers
gas
centelleador
fibra
óptica
foto
sensor
Optical PPAC
Jornada PROMESA, 30 de October de 2025
Notes: 10
10

## Slide 11
Micro-machining
lab.
Radioprotected
area
Control
room
Laser lab.
Instrumentation lab.
X-ray
station
proton
Exp.
Laser
clean room
Facilities:
- Alpha 10/XS laser from Thales.
- Clean room.
- Radioprotected acceleration area.
- Instrumentation and laser labs.
José Benlliure
Two laser lines:
- 1 mJ, 1 kHz, 35 fs for X-ray generation
- 1 J, 10 Hz, 25 fs for proton acceleration
Laser Laboratory for Acceleration and Applications
Control
room
11
Jornada PROMESA, 30 de October de 2025
Notes: 11
11

## Slide 12
Laser-accelerated ions at CLPU
José Benlliure
Beam times at CLPU (October 2022, May 2024):
Laser-induced neutron generation.
Ion acceleration with the L2A2 wheel target.
11C production with a 1 PW laser system.

## Slide 13
Laser-accelerated ions at CLPU
José Benlliure
Multi-shot ion acceleration.
13

## Slide 14
Laser-plasma acceleration could be the enabling technology to produce in-house on-demand doses of PET probes of interest at low cost, in an automated, user-friendly device. The compact size of laser-plasma accelerators would reduce the capital cost of the accelerator and the required infrastructures, in particular radiation shielding.
Similar arguments are also valid for the production of radio-nuclides of interest for medical applications other than PET, e.g. 226Rd(g,n)225Rd-->225Ac
José Benlliure
Radioisotope production for PET-imaging
14
Jornada PROMESA, 30 de October de 2025

## Slide 15
11C isotope production
Using the 1PW VEGA system, energies are sufficient to produce 11C through proton-induced reactions on Boron, 11B(p,n)11C.
A compact setup was developed to enable irradiation of an activation sample and measure its activity in vacuum conditions (no need for let-up).
Measurements based on coincidence detection (only measurements of β+ decays).
L2A2
CLPU
natB
CsI
Production of 11C at CLPU
José Benlliure
Activation measurements
15
Jornada PROMESA, 30 de October de 2025

## Slide 16
Demonstrated continuous 11C production in multi-shot operation (series of 20 shots at 0,1 Hz).
Reproducing the decay curve and half-life of 11C.
Achieved activities above 10 kBq per shot.
Production of 11C at CLPU
On the path to generate pre-clinical activity levels using laser-driven sources
José Benlliure
T1/2 = 1221,8 s
Experiment 2022
J. Peñas et al., Scientifc Reports, 14, 11448 (2024)
16
Laser energy [J] | Repetition Rate [Hz] | # shots | Activity per shot [kBq] | Total activity [kBq]
12 | 0,2 | 40 | 1.8 | 68.6
20 | 0,1 | 10 | 3.2 | 31.5
25 | 0,1 | 20 | 12.4 | 233.8
Jornada PROMESA, 30 de October de 2025

## Slide 17
Target operation @ 1Hz, 1PW
Production of 11C at CLPU
Experiment 2024: laser-driven proton source @ 1 Hz, 1 PW
Continuous activation over long series of shots (~800) was achieved.
The present bottle-neck for a continuous proton source driven by PW laser systems is the heating of the optics.
1 Hz
0,2 Hz
Expected 1 Hz
> 4MBq!
At 0,2 Hz the laser optics have time to cool between shots.
At 1 Hz the heating of the optics reduces the proton energy and then the final activities.
17
José Benlliure
Jornada PROMESA, 30 de October de 2025

## Slide 18
Target operation @ 1Hz, 1PW
Perspectives for the laser production of 11C
José Benlliure
PW laser systems are probably not the most cost efficient solution for the production of 11C.
Compact ~100 TW systems at 100 Hz could represent a good option.
18
Jornada PROMESA, 30 de October de 2025

## Slide 19
José Benlliure
Numerous studies have demonstrated the efficacy of the use of high dose rates in reducing radiotoxicity in healthy tissues.
Michael Seimetz
Ana Vega
José Benlliure
Laser accelerators naturally produce ultra-short particle pulses that meet the requirements of flash radio-therapy and do not require a gantry.
 | Total dose | Dose rate
Conventional therapy | 1-10 Gy | 1 Gy/min
Flash therapy | 1-10 Gy | > 10 Gy/s
Radiobiology studies with laser accelerated particles
In-vitro studies of flash effect

## Slide 20
José Benlliure
The benefit of flash radio-therapy seems to be accepted but, there are still many parameters that should be optimised:
Type of radiation: electrons, protons, …
Dose rate (> 10 Gy/s).
Pulse duration and number:
 100 pulses of 0,1 Gy in 1 ms: 10 Gy with 102 Gy/s.
 1000 pulses of 0,01 Gy in 1 ms: 10 Gy with 104 Gy/s.
Time between pulses.
Michael Seimetz
Ana Vega
José Benlliure
Radiobiology studies with laser accelerated particles
In-vitro studies of flash effect

## Slide 21
José Benlliure
Michael Seimetz
Ana Vega
José Benlliure
Proof of concept with X rays at L2A2, Nov. 2021:
Cell culture and transport.
Dose determination.
Irradiation protocol.
Analysis procedures.
Irradiations with protons at CLPU, Oct. 2023:
Selection of the proton energy.
Precise determination of the dose.
A. Reija: PhD USC (prev. 2025).
Radiobiology studies with laser accelerated particles
In-vitro studies of flash effect
21
Human lung adenocarcinoma cells
Notes: 21
21

## Slide 22
Phase contrast imaging
José Benlliure
Objects exposed to a radiation field not only cause radiation absorption, but also a phase shift.
Information on the phase shift can be retrieved from the intensity variations due to the interference pattern created by the refraction produced by the phase shift. However, a X-ray source with high transverse coherence is required.
For materials with low absorption (e.g. biological matter) the phase shift can gives orders of magnitude stronger contrast than absorption.
s: source size
R: source-detector distance
d: source-sample distance
z: sample-detector distance
Transverse coherence can be obtained with small size sources or large source-to-sample distance (Fresnel approximation).
Laser-induced X-ray sources fulfill the conditions for phase-contrast imaging: small size sources (~10 mm) and high fluxes.
b: absorption refraction index.
d: phase shift refraction index.
Tomographic image of anatomical features of a live mouse.
22
Jornada PROMESA, 30 de October de 2025
Notes: 22
22

## Slide 23
José Benlliure
A. Coathup: PhD USC (prev. 2025).
23
Phase contrast imaging
A compact kHz X-ray source running on air.
Laser parameters: ~ 1 mJ, 35 fs, 1kHz.
Target material: 100x100x1 mm3 copper plates, beam focus sxy~2 mm.
Target replenishment: shot-by-shot moving plate along concentric circles of impacts (two linear and one rotating stages).
Jornada PROMESA, 30 de October de 2025

## Slide 24
José Benlliure
Laser-induced X-ray 2D phase-contrast imaging
Phase Retrieval
Amplitude Retrieval
  Phase retrieval algorithm
  - Propagation-based phase-contrast imaging.
  - Single image at one source-to-object distance.
  Assumptions:
  - Not negligible absorption
  - δ and μ are proportional
  - Fresnel approximation
Dried insect material:
- Chitin ( C8H13NO5)
- µ = 7,015 mm-1 δ = 1.38 x 10-5
- Magnification = 1,21
- d = 62 mm z = 13 mm
Phase-contrast imaging provides a better contrast compared to amplitude imaging.
24
Jornada PROMESA, 30 de October de 2025
Notes: 24
24

## Slide 25
Contribution to the next PROMETEO proposal
José Benlliure
Construction and commissioning of advanced target assemblies for the continuous operation of laser accelerators to be used in compact generators of medical radio-isotopes and advanced systems for phase-contrast X-ray imaging.
25
Objective
1 hour operation.
Continuous
operation.
15 minutes operation.
Notes: 25
25

## Slide 26
Contribution to the next PROMETEO proposal
José Benlliure
Phase 1: Commissioning of the tape-drive target existing at L2A2.
Phase 2: Construction of a target characterization system.
Phase 3: Design, construction and commissioning of a liquid-jet target.
Phase 4: First experiments with the targets: X-ray and 11C production.
26
Working plan
Notes: 26
26

## Slide 27
Contribution to the next PROMETEO proposal
José Benlliure
Equipment:
- Vacuum chamber and associated pumping system: 75 k€ (other call)
- Target characterization system: 20 k (this call)
- Liquid-target assembly: 25 k€ (this call)
Consumables: 15 k€ (another call)
Personnel
- 3 years PhD contract: 75 k€ (this call)
Travels: 15 k€ (this call)
27
Funding request
We intend to set up a new laboratory at IFIC to develop key laser-plasma acceleration technologies relevant for medical applications. Our needs are as follows:
Notes: 27
27

## Slide 28
TOF signals
Proton Spectra
Alingment beam
IR beam
Proton beam
OAP F/2
Time-of-flight detector
Intensity on target 0.1 – 1.5 x 10 21 W/cm2
Target holder
Laser-accelerated ions at L2A2
José Benlliure
28
Notes: The first peak appearing in the TOF signals is the gamma flash, which englobes all the radiation produced in the interaction, and marks the zero time.
The second peak represents the protons arrival some ns after the interaction, with the time and space we can obtain the energy of the protons.
Moreover, the calibrated TOF detector give us also de number of proton per shot in an online configuration.
The first experimental results at the L2A2 are 10^10 protons per shot up to 1.5 MeV obtained not with best parameters possible.
Working with suitable laser and target parameters the L2A2 facility should produce 10^12 protons per shot up to 10 MeV.

## Slide 29
High power laser systems
José Benlliure
Ultra intense laser pulses (I>5 1018 W/cm2):
Lasers are pulsed with relatively low frequency: large peak power and modest average power.
The intensity of the pulses depends on three parameters: energy, time and surface.
High energy laser systems:
E ~ 1 KJ - 1 MJ, t ~ 1 ps, A~0.1 mm2
Ultra-short laser pulses:
E ~ 1 J - 10 J, t ~ 10-100 fs, A~1 mm2
29
Two approaches are used to produce ultra intense laser pulses:

## Slide 30
José Benlliure
Replenishing and positioning of the acceleration target
The target material used to accelerate the ions (~ 1 mm Al) volatilises after each impact of the laser pulses and has to be replaced and positioned with an accuracy better than 10 mm every 100 ms (10 Hz).
30
1 hour operation.
Continuous
operation.
3D mapping of impact positions on the target enables an accurate positioning.
~10 mm
J. Peñas: PhD USC (2023).
J. Peñas et al., HPLE 11, e22 (2024)
High-repetition rate targets
15 minutes operation.
Notes: 30
30

## Slide 31
Target operation @ 1Hz, 1PW
Several improvements on the wheel to minimize impact of EMP.
  Relay system to physically disconnect the motors and controller during the shots.
Production of 11C at CLPU
Experiment 2024: laser-driven proton source @ 1 Hz, 1 PW
The operation of the target is stable at 1 Hz but the laser cannot keep up at such rates because of the heating of the optics.
Electromagnetic
pulse (EMP)
A continuous reduction of the proton energy is observed.
José Benlliure
31