## Slide 1: IFMIF-DONES: Status and Overview of a Next-Generation High-Current Accelerator Facility for Fusion Materials Qualification
J. Maestre on behalf of the DONES Integrated Programme Team
Red Española de Futuros Colisionadores
20/10/2026

## Slide 2: Outline
Description of IFMIF-DONES core
Summary
Intro to IFMIF-DONES
Accelerator Systems
DONES- Experimental Capabilities
Lithium Systems
Test Systems

## Slide 3: Why IFMIF-DONES ?
One of the main differences between ITER and DEMO is the radiation dose: at DEMO more than
two orders of magnitude higher
1-3 dpa/lifetime
20-50 dpa/lifetime

## Slide 4: What is IFMIF-DONES?
Heat removal by high velocity Li flux
Stripping reaction
15
A neutron flux of ~5 1014 n/ cm2/s
is generated with a neutron spectrum up to 55 MeV energy
An accelerator based fusion-like neutron source
to be used for the qualification of the materials to be used in the DEMO Reactor
High Flux Test Module requirements
Dpa | 20 dpaNRT (<2.5 years, 300 cm3) 50 dpaNRT (<3 years,100 cm3)
Temperature | Controlled 250 – 550 C
Dpa gradient | <15% (gauge volume)
Temperature gradient | <3% (gauge volume)
Facility able to irradiation multiple irradiation modules simultaneously

## Slide 5: IFMIF-DONES Facility
The site is located at Escúzar -18 km southwest from Granada city- Spain
European Strategic Facility RI Project
High priority facility in the EU Fusion Roadmap

## Slide 6: IFMIF-DONES Facility
Site, Building & Plant Systems
3.2- Main Building
CICS
70% Availability
30 years Operation
Accelerator Vault
Lithium Systems
Access Cell
RF area
TIR
Complementary experiments area
Test Cell (Target + Test Systems)

## Slide 7: DONES Programme Governance
  Observers:
  Czech Republic
  Finland
  France
  Germany
  Hungary
  Latvia
  Lithuania
  Poland
  Romania
  Slovakia
  Ukraine
Current Parties
  F4E
  IFMIF-DONES España (Host)
  INFN
  QST
  RBI
Signature of the
Multilateral International DONES Agreement
MIDA
21st November 2025

## Slide 8: Outline
Description of IFMIF-DONES core
Summary
Intro to IFMIF-DONES
Accelerator Systems
DONES- Experimental Capabilities
Lithium Systems
Test Systems

## Slide 9: The 5 MW deuteron LINAC
Highest D+ current LINAC
One of the highest average beam power & perveance
Top H+ & D+ Injector performance
Longest RFQ
High Beam loading in resonant cavities
Record of light hadrons current through SC cavities
40 MeV / 125 mA CW / 5 MW SC LINAC
Facility (Accelerator, target…) design considering feasibility upgrading to 10 MW!

## Slide 10: Accelerator Systems: parameters
175 MHz SSPA RF Stations
20x5 cm2 footprint
(reference)
10x5 cm2 footprint
(optional)
Ancillaries
Vacuum, Cryogenics, Water cooling, Gas and electric distribution…
D+ CW 175 MHz SC LINAC
125 mA / 40 MeV  5 MW
Total length of ~100 m
Windowless liquid Li target
, 87% availability
Hands-on maintenance (<1 W/m)
Target-beam at 9° angle 
possibility to upgrade
with 2nd mirror accelerator (10 MW)
Independent EMC mesh
embedded into the Building
Beam footprint @ target

## Slide 11: Accelerator Systems: description
ECR ion source – SILHI type
Validated in LIPAc at nominal CW current
Chopper for high intensity pulsed D+ beam
INJECTOR / LEBT
RFQ
MEBT
SRF LINAC
HEBT
Main functions
Generate D⁺ ions; extract and accelerate them to 100 keV; focus and match the beam transversely to the RFQ. Diagnostics support tuning of current, profile and emittance.
Beam operation: continuous-wave (CW) nominally; injector/LEBT can support commissioning and pulsed modes.
EXTRACTED BEAM
100 keV / 140 mA
DC design point
ION SOURCE
2.45 GHz ECR
Deuterium plasma
BEAM AT RFQ
125 mA
Nominal accelerator current

## Slide 12: Accelerator Systems: description
Main functions
INJECTOR / LEBT
RFQ
MEBT
SRF LINAC
HEBT
The RFQ simultaneously bunches, focuses and accelerates the high-current beam
FOUR-VANE COPPER CAVITY
Bunching + acceleration + transverse focusing
RF FREQUENCY
175 MHz
CW operation
ENERGY GAIN
0.1 → 5 MeV
Deuterons
STRUCTURE LENGTH
≈ 9.7 m
Four-vane copper RFQ
BEAM CURRENT
125 mA
Nominal output
BEAM POWER AT EXIT
625 kW
5 MeV × 125 mA
RF design and validation
One of the longest and highest power RFQ
Loss control: High-current CW operation makes beam loss a major activation and reliability concern. The RFQ uses careful field shaping and cooling to control thermal loading.
Optimization from LIPAc feedback

## Slide 13: Accelerator Systems: description
INJECTOR / LEBT
RFQ
MEBT
SRF LINAC
HEBT
Main functions
Match the RFQ output beam to the longitudinal and transverse acceptance of the SRF linac.
BEAM ENERGY
5 MeV
RFQ output
BEAM CURRENT
125 mA
CW
BEAM-DYNAMICS LENGTH
≈ 2.35 m
Nominal design
RE-BUNCHER VOLTAGE
up to 350 kV
Effective voltage
TRANSMISSION TARGET
> 99.9%
MEBT input to output
Quadrupole magnets transport and match the beam envelope. Scrapers intercept halo and particles outside the accepted phase space. Two five-gap re-buncher cavities adjust bunch phase and energy spread for efficient capture by the superconducting cavities.
Optimization from LIPAC feedback: Improvement on maintenance and beam diagnostics; rad-hard and low activation materials.
MEBT design and validation
VATIAC Validator under manufacturing
First operational tests on-site in 2028
Status

## Slide 14: Accelerator Systems: description
Main functions
Five cryomodules provide the main acceleration from 5 to 40 MeV
SRF design
Accelerating structures
Niobium half-wave resonators (HWRs), two types: 19 x low-β and 27 x high- β
Focusing & cryogenics
Superconducting solenoids provide focusing. The cryostat maintains cavities at cryogenic temperature and provides thermal and magnetic shielding
INJECTOR / LEBT
RFQ
MEBT
SRF LINAC
HEBT
SUPERCONDUCTING HWRs
CM1
HWR
CM2
HWR
CM3
HWR
CM4
HWR
CM5
HWR
5 MeV
40 MeV
FINAL ENERGY
40 MeV
Deuterons
BEAM CURRENT
125 mA
CW nominal
OUTPUT BEAM POWER
5 MW
40 MeV × 125 mA
CRYOMODULES
5
Warm sections between
OPERATING TEMPERATURE
≈ 4.5 K
Liquid-helium cooled
Validation: Assembly of the LIPAc Cryomodyule ongoing  first beam expected in 2027

## Slide 15: Accelerator Systems: description
INJECTOR / LEBT
RFQ
MEBT
SRF LINAC
HEBT
Main functions
Transport, shape and deliver the 5 MW beam to the lithium target — or to the beam dump
HEBT design
Beam shaping
Magnetic elements and scrapers shape the beam into a quasi-rectangular footprint on the lithium free surface; the footprint is adjustable to support commissioning and operation.
Commissioning
The line transports the beam to the lithium target in normal operation and can direct it to the high-power beam dump (HPBD) during commissioning or when target operation is unavailable.
INPUT ENERGY
40 MeV
From SRF linac
NOMINAL CURRENT
125 mA
CW
BEAM POWER
5 MW
High-power transport
FOOTPRINT RANGE
10–20 cm × 5 cm
Horizontal × vertical
TARGET INCIDENCE
≈ 9°
On lithium jet
FROM SRF
DIPOLES / QUADS
SCRAPERS & DIAGNOSTICS
TARGET / HPBD
Some features
Multipole magnets (oct/dodec) for rectangular shape
High Power Beam Dump for commissioning and tuning (1% DC)
Safety-credit module containing Fast valves
Aluminium beampipe to minimize the activation
Water-cooled RH Scraper
He-cooled RH Collimator at TIR
Beam diagnostics for all beam modes
Secondary beamline for 2nd accelerator with target diagnostics
VATIAC Validator under manufacturing
First operational tests on-site in 2028
Status

## Slide 16: Lithium Systems
Main functions
To generate a stable liquid lithium target for enabling D-Li stripping reaction and producing an adequate neutron flux to properly irradiate
LS design
Target System: To provide a continuous Li jet whose interaction with D+ beam generates the Neutron flux.
Heat Removal Loop: To remove the energy deposition on the Lithium.
Impurity Control System: To localize and control the impurities in the Lithium.
beam
TARGET
HEBT
BEAM POWER
5 MW
High-power transport
FOOTPRINT RANGE
10–20 cm × 5 cm
Horizontal × vertical
TARGET FLOW
100 L/s
lLithium Loop
TARGET JET VELOCITY
15 m/s
On lithium jet

## Slide 17: Test Cell & Target
Beam
TEST CELL
Target System is allocated inside Test Cell, concrete cell covered by a stainless-steel liner under a controlled environment (He or Ar).
The TC confine the neutron source and allocate the different irradiation modules
TARGET
Converts the high-power deuteron beam into an intense neutron field
Liquid metal target
Windows-less
Under vacuum (10^-4 mbar)
Heat flux: 100 KW/cc
Jet thickness: 25 ± 1 mm
Li inlet T: 300 °C
Li velocity: 15 m/s
Chamber pressure: 10-2 Pa
SSTT specimens
HFTM assembly (316LN)
F. Arbeiter (KIT)
Irradiation Modules (HFTM)
Irradiation device positioned immediately behind the lithium target. It houses small specimens of candidate fusion-reactor materials in dedicated irradiation capsules, exposing them to a high-intensity neutron field

## Slide 18: Outline
Description of IFMIF-DONES core
Summary
Intro to IFMIF-DONES
Accelerator Systems
DONES- Experimental Capabilities
Lithium Systems
Test Systems

## Slide 19: Facility & users
Area for complementary experiments with continuous neutron beam
Three main experimental areas – First Experimental Programme to be presented this year
Test cell – Main neutron experimental area (fusion users)
Area for complementary experiments with deuteron beam
Design of TOF DONES ready (CIEMAT/NFUS)
Fusion users (materials, breeding blankets,…)
Nuclear physics
Astrophysics
Medical applications
Industry, safety
Societal applications
WS DONES Users – CIEMAT- Madrid – 13-15 October
https://indico.ifmif-dones.es/event/92/
< 2 ns microbunches
Challenge  40 MeV extraction system based on meander kickers
Neutron Beam Tube and Shutter connected to the Target Area (Test Cell)
>1010 n/cm2-s

## Slide 20: Test cell – High Flux Irradiation Module
Baseline focused on High Flux Test Module (HFTM): high-priority structural materials irradiation.
Two mature module designs: one exposes material specimens; the other characterizes the neutron/radiation field.
HFTM
High Flux Test Module
• Mission: irradiate small structural-material specimens, initially Eurofer (9% Cr steel).
• Peak neutron flux: up to 5 × 10¹⁴ n·cm⁻²·s⁻¹.
• Controlled specimen temperature: 250–550 °C (target spread about ±3%).
• Damage objective: 13-35 dpa/fpy up to 300 cm³ (22-50 dpa/fpy with two accelerators)
10-15 appm He / dpa, 45-55 appm H / dpa.
Samples:
Steel Eurofer 97: First Wall Fusion Structural materials
Copper: divertor heat sink
Tungsten: Armor
STUMM
Start-up Monitoring Module
• Mission: map radiation fields behind the target, especially during commissioning.
• Diagnostics cover neutron flux and radiation-field characteristics.
• Designed for transient and steady-state monitoring.
• STUMM-PROTO development includes ~35 m coaxial cables to emulate remote electronics.
Sensors:
Micro-fission Chambers: fast neutrons
Ionization Chambers: they help separate the neutron contribution from the combined neutron–gamma signal
(SPNDs: Alternative or complementary detectors for thermal and epithermal neutron flux
Gamma thermometers: Measures nuclear heating
SSTT specimens
F. Arbeiter (KIT)

## Slide 21: Test cell – Other Irradiation Modules
BLUME • LBVM • TRTM: not yet explicitly part of the facility baseline
Three complementary concepts target functional materials and blanket sub-systems beyond the baseline high-flux structural-material programme.
BLUME
Blanket Functional Material Module
• Representative section of the Helium-Cooled Pebble-Bed (HCPB) blanket breeder zone.
• Focus: blanket functional materials and integrated unit-size structures.
• Helps assess blanket technology under fusion-like neutron exposure.
CONCEPTUAL DESIGN
LBVM
Liquid Breeder Validation Module
• Targets liquid-breeder R&D, especially PbLi and associated functional materials.
• Can investigate anti-corrosion / anti-permeation barriers.
• Concept links to liquid PbLi blanket concepts, including WCLL.
CONCEPTUAL DESIGN
TRTM
Tritium Release Test Module
• Designed for lithium-ceramic pebble beds associated with the HCPB blanket.
• Measures/validates tritium release behaviour under irradiation.
• Concept also includes neutron-multiplier materials such as beryllides.
CONCEPTUAL DESIGN
Figures extracted from: Arbeiter, Frederik, et al. "The IFMIF-DONES irradiation modules." Nuclear Fusion 65.12 (2025): 125001.

## Slide 22: DONES Timeline

## Slide 23: Outline
Description of IFMIF-DONES core
Summary
Intro to IFMIF-DONES
Accelerator Systems
DONES- Experimental Capabilities
Lithium Systems
Test Systems

## Slide 24: Summary
IFMIF-DONES is a key step towards reducing material-related uncertainties and enabling the development of reliable fusion energy
IFMIF-DONES will provide a unique accelerator-based neutron irradiation facility for both fusion but also non-fusion applications
IFMIF-DONES is an international Facility right now under Construction Phase
Procurement of the LINAC and Test Cell are ongoing with several systems under final design and manufacturing

## Slide 25
Thank you for your attention…
www.ifmif-dones.es